## Slide 1: Confined Space Training

## Slide 2: Disclaimer
Confined Space Training
This material was produced under
grant number SH-05073-SH8 from
the Occupational Safety and Health Administration, U.S. Department of Labor.
It does not necessarily reflect the views or policies of the U.S. Department of Labor, nor does mention of trade names, commercial products, or organizations imply endorsement by the U.S. Government.

## Slide 3: Welcome
Confined Space Training
What is a Confined Space
When does it become Permit Required?
What are the Hazards
Training

## Slide 4: Module-1
Confined Space Training
What is a Confined Space
When does it become Permit Required?
What are the Hazards
Training

## Slide 5: What is a Confined Space
According to OSHA
29 CFR 1910.146b
A Confined Space is defined as:
Large enough and so configured that a worker can bodily enter it, and
Has limited or restricted means of entry or exit, and
Is not designated for continuous worker occupancy.
https://www.osha.gov/laws-regs/regulations/standardnumber/1910/1910.146

## Slide 6: What is a Confined Space – Part 2
According to OSHA
29 CFR 1910.146b
A confined space is defined as:
Large enough and so configured that a worker can bodily enter it, and
Has limited or restricted means of entry or exit, and
Is not designated for continuous worker occupancy.
https://www.osha.gov/laws-regs/regulations/standardnumber/1910/1910.146
NOTE: What is considered ENTRY?
If you break the plane of a confined space, you have entered the confined space!

## Slide 7: Module-1b
Confined Space Training
What is a Confined Space
When does it become Permit Required?
What are the Hazards
Training

## Slide 8: When does it become Permit Required?
Permit Required Confined Space has one or more of the following characteristics:
1. Contains or has the potential to contain a hazardous atmosphere;
2. Contains a material that has the potential for engulfing an entrant;
3. Has an internal configuration such that an entrant could be trapped or asphyxiated by inwardly converging walls or by sloped/tapered floors.

## Slide 9: When does it become Permit Required? – Part 2
Example of a
permit-required confined space.

## Slide 10: When does it become Permit Required? - Part 3
Permit-required confined space entry
Permit is required whenever there is a hazard
Or potential hazard

## Slide 11: Module-3
Confined Space Training
What is a Confined Space
When does it become Permit Required?
What are the Hazards
Training

## Slide 12: What are the Hazards?
Potential Hazards in Confined Spaces
Asphyxiating - Oxygen Deficiency
  <19.5% or >23.5% oxygen concentration
CO2
  CO2 is toxic in higher concentrations:
    1% (10,000 ppm) will make some people feel drowsy.
    Concentrations of 7% to 10% cause dizziness, headache, visual and hearing dysfunction, and unconsciousness within a few minutes to an hour.
Toxic Materials
  Carbon Monoxide
  Hydrogen Sulphide
  Welding fumes
  Corrosives
Mechanical Hazards
  Mixers
  Crushers
  Engulfment
  Soil around an excavation
  Grain in a silo
  Powdered material in a bin

## Slide 13: What are the Hazards? – Part 2
Potential Hazards in Confined Spaces
Electricity
Flammable -Combustibles
  Methane
  Hydrogen
  Acetylene
  Propane
  Gasoline fumes
Asphyxiating - Oxygen Deficiency
  <19.5% or >23.5% oxygen concentration
CO2
  CO2 is toxic in higher concentrations:
    1% (10,000 ppm) will make some people feel drowsy.
    Concentrations of 7% to 10% cause dizziness, headache, visual and hearing dysfunction, and unconsciousness within a few minutes to an hour.
Toxic Materials
  Carbon Monoxide
  Hydrogen Sulphide
  Welding fumes
  Corrosives
Mechanical Hazards
  Mixers
  Crushers
Engulfment
  Soil around an excavation
  Grain in a silo
  Powdered material in a bin
Oxygen could be removed from the air in a confined space by:
Material in the space could displace the oxygen
Rusting could create a chemical reaction that uses up the oxygen
The space could be purged with a gas to prevent explosions.

## Slide 14: What are the Hazards? – Part 3
Gasses

## Slide 15: What are the Hazards? – Part 4
Combustibility

## Slide 16: What are the Hazards? – Part 5
Engulfment

## Slide 17: What are the Hazards? – Part 6
Mechanical

## Slide 18: What are the Hazards? – Part 7
Biological

## Slide 19: What are the Hazards? – Part 8
Chemical

## Slide 20: What are the Hazards? – Part 9
Extreme
Temperatures

## Slide 21: What are the Hazards? – Part 10
Hazards from
Animals

## Slide 22: Module-4
Confined Space Training
What is a Confined Space
When does it become Permit Required?
What are the Hazards
Training

## Slide 23: Confined Space Training
OSHA 1910.146(g) Training
The employer shall provide training so that all employees whose work is regulated by this section acquire the understanding, knowledge, and skills necessary for the safe performance of the duties assigned under this section.

## Slide 24: Confined Space Training – Part 2
OSHA 1910.146(g) Training
Training shall be provided to each affected employee:
  Before the employee is first assigned duties under this section;
  Before there is a change in assigned duties;
  Whenever there is a change in permit space operations that presents a hazard about which an employee has not previously been trained;
  Whenever the employer has reason to believe either that there are deviations from the permit space entry procedures.

## Slide 25: Confined Space Training – Part 3
Entry:
The action by which a person passes through an opening into a permit-required confined space; Entry includes ensuing work activities in that space and is considered to have occurred as soon as any part of the entrant’s body breaks the plane of an opening into the space.
Confined Space Entry

## Slide 26: Confined Space Training – Part 4
Authorized Entrant
  Enters the confined space
Authorized Attendant
  Stands watch outside the entry point of the space
Entry Supervisor
  Oversees entry, ensures conformity to permit & acceptable conditions for entry
Confined Space Personnel

## Slide 27: Confined Space Training – Part 5
Authorized Entrant
The employee who will physically enter the confined space to perform the work.
Confined Space Personnel

## Slide 28: Confined Space Training – Part 6
Authorized Attendant
The employee who remains outside the confined space and;
  monitors the entrant(s)
  guards the space against unauthorized entry
  warns the entrants of any unusual conditions
  and summons the rescue personnel if needed.
Confined Space Personnel

## Slide 29: Confined Space Training – Part 7
Entry Supervisor
The employee who remains outside the confined space and;
  warns the entrants of any unusual conditions
  Completes Permits,
  ensures conformity to permit & acceptable conditions for entry
Confined Space Personnel

## Slide 30: Confined Space Training – Part 8
Confined Space Permits

## Slide 31: Confined Space Training – Part 9
Confined Space Permits

## Slide 32: Confined Space Training – Part 10
Confined Space Permits

## Slide 33: Confined Space Training – Part 11
Confined Space Permits

## Slide 34: Confined Space Training – Part 12
Prior to every entry when the space is vacant;
After a 10-minute ventilation period (if ventilation is necessary);
At least hourly for permit-required confined spaces. NOTE: A good practice is to re-test the atmosphere after breaks or having been out of the confined space for a period of time.
More frequently, if conditions or suspicions warrant.
Confined Space Permits
Atmosphere Testing Must Be Performed

## Slide 35: Confined Space Training – Part 13
Prior to every entry when the space is vacant;
After a 10-minute ventilation period (if ventilation is necessary);
At least hourly for permit-required confined spaces. NOTE: A good practice is to re-test the atmosphere after breaks or having been out of the confined space for a period of time.
More frequently, if conditions or suspicions warrant.
Confined Space Permits
Atmosphere Testing Must Be Performed

## Slide 36: Confined Space Training – Part 14
  Procedures clearly spelled-out.
  Rescue teams made available, Means of contact provided.
  Appropriate equipment available; retrieval systems for non-entry rescue; vertical >5 ft.
  In-house rescue teams are OPTIONAL!
  Dial 911 & notify of confined space emergency, you may attempt retrieval at that point.
Evacuation & Rescue

## Slide 37: Confined Space Training – Part 15
for each affected employee
before first assignment & with changes
deviations from space entry procedures
shall establish employee proficiency
Training: Must Be Certified In Writing

## Slide 38: Confined Space Training – Review

## Slide 39: Knowledge Check
What is a Confined Space?

## Slide 40: Knowledge Check – Part 2
What is a Confined Space?
A Confined Space is defined as:
Large enough and so configured that a worker can bodily enter it, and
Has limited or restricted means of entry or exit, and
Is not designated for continuous worker occupancy.

## Slide 41: Knowledge Check – Part 3
2. What is a Permit Required Confined Space?

## Slide 42: Knowledge Check – Part 4
2. What is a Permit Required Confined Space?
Permit Required Confined Space has one or more of the following characteristics:
1. Contains or has the potential to contain a hazardous atmosphere;
2. Contains a material that has the potential for engulfing an entrant;
3. Has an internal configuration such that an entrant could be trapped or asphyxiated by inwardly converging walls or by sloped/tapered floors.

## Slide 43: Knowledge Check – Part 5
3. Who are the Qualified workers?

## Slide 44: Knowledge Check – Part 6
3. Who are the Qualified workers?
The Supervisor – trained, competent, fills in permits, supervises the work & terminates the entry if needed or when completed
The Entrant – trained & authorized to enter. Performs the work.
The Attendant – trained & authorized

## Slide 45: Knowledge Check – Part 7
4. What is the primary reason for using a retrieval system for work within a Permit Required Confined Space?

## Slide 46: Knowledge Check – Part 8
4. What is the primary reason for using a retrieval system for work within a Permit Required Confined Space?
To allow the attendant to perform a Non-Entry Rescue if problems develop during the entry.
NOTE: Because of the inherent dangers of this work, Only a Trained and Authorized Rescue Team can enter to assist the Entrant (worker)

## Slide 47: Additional Resources
OSHA website: http://www.osha.gov and OSHA offices: Call or Write (800-321-OSHA)
Compliance Assistance Specialists in the area offices
National Institute for Occupational Safety and Health (NIOSH) – OSHA’s sister agency
OSHA Training Institute Education Centers
Public libraries