## Slide 1
Moving large, heavy loads is crucial to today's manufacturing and construction industries.
Much technology has been developed for these operations, including careful training and extensive workplace precautions.
There are significant safety issues to be considered, both for the operators of the diverse "lifting" devices, and for workers in proximity to them.

## Slide 2
RIGGING fundamentals
Presented By: HENNEPIN TECHNICAL College in partnership with Federal OSHA Susan Harwood Grant
This material was produced under Grant # SH-19496-09-60-F-27 from the OSHA, U.S. Dept of Labor. It does not necessarily reflect the views or policies of the U.S. Dept of Labor, nor does mentioning of trade names, commercial products, or organizations imply endorsement by the U.S. Government.

## Slide 3: Course Introduction
Instructor(s)
Classroom
  Restrooms
  Emergency Exits
Breaks
Introduction to TurningPoint

## Slide 4: TurningPoint

## Slide 5: R _ G _ I _ G
N I G
E J W
I B B
C E X

## Slide 6: Rigging Fundamentals

## Slide 7: Why are we here?
Rigging Fundamentals

## Slide 8: Why Are We Here?
Crane and Rigging Accidents
  An annual average of 22 construction workers were killed in crane-related incidents from 1992 to 2006, according to The Center for Construction Research and Training.
OSHA regulations and standards
Because we care about you, your co-workers, and your families.
  Everyone is entitled to go home from work, EVERY DAY!

## Slide 9: Occupational Safety and Health Administration (OSHA)
Code of Federal Regulations (29 CFR):
  General Duty Clause:
    (a) Each employer
      (1) shall furnish to each of his employees employment and a place of employment which are free from recognized hazards that are causing or are likely to cause death or serious physical harm to his employees;
      (2) shall comply with occupational safety and health standards promulgated under this Act.

## Slide 10: Occupational Safety and Health Administration (OSHA)
Code of Federal Regulations (29 CFR):
  General Duty Clause:
    (b) Each employee shall comply with occupational safety and health standards and all rules, regulations, and orders issued pursuant to this Act which are applicable to his own actions and conduct.

## Slide 11: 29 CFR Occupational Safety and Health Regulations (OSHA Standards)
  1910; Occupational Safety and Health Standards
Subpart N: Materials Handling and Storage
  1910.179 - Overhead and gantry cranes.
  1910.180 - Crawler locomotive and truck cranes.
  1910.184 - Slings.
1926; Safety and Health Regulations for Construction
Subpart N: Cranes, Derricks, Hoists, Elevators, and Conveyors
  1926.251 - Rigging equipment for material handling.
  1926.550 - Cranes and derricks.

## Slide 12: American Society of Mechanical Engineers (ASME)
Standards
  B30.9: Slings
  B30.10: Hooks
  B30.16: Overhead Hoist Underhung
  B30.20: Below the Hook Lifters
  B30.21: Lever Hoist
  B30.26: Rigging Hardware

## Slide 13: Definition of Terms
Rigging Fundamentals

## Slide 14: Overhead lifting refers to an object raised more than six feet above the ground.
True
False

## Slide 15: Overhead Lifting
“Process of lifting that would elevate a freely suspended load to such a position that dropping a load would present a possibility of bodily injury or property damage.”

## Slide 16: Working Load Limit (W.L.L.)
The MAXIMUM load that shall be applied in direct tension to undamaged straight length of a sling or hoisting equipment

## Slide 17: The Working Load Limit [WLL] is ____ of the rigging equipment.
Less than the breaking strength
Equal to the breaking strength
Greater than the breaking strength

## Slide 18: Design Factor
A ratio of the breaking strength to the working load limit
  Example: If a chain sling has a breaking strength of 28,400# and a W.L.L. of 7,100#; it would have a design factor of 4:1

## Slide 19: Design Factor
Component | Minimum Design Factor
Nylon rope sling | 5:1
Polyester rope sling | 5:1
Polypropylene rope sling | 5:1
Alloy steel chain sling | 4:1
Wire rope sling | 5:1
Metal mesh sling | 5:1
Synthetic web sling | 5:1
Synthetic round sling | 5:1

## Slide 20: Elongation
The ability of a piece of load bearing material to permanently increase in length before it fails or breaks
  Expressed as a percentage of increase over its original length

## Slide 21: Reach
The distance measured from the top of the master link to the bowl of the load hook.

## Slide 22: Sling Hitches
Vertical

## Slide 23: Sling Hitches
Vertical
Choker

## Slide 24: Sling Hitches
Vertical
Choker
Basket

## Slide 25: Who Are These People?
Designated person
Competent person
Qualified person

## Slide 26: OSHA Says…
The term "designated" personnel means selected or assigned by the employer or the employer's representative as being qualified to perform specific duties.

## Slide 27: OSHA Says…
Competent Person
29 CFR 1926.32(f) states: "Competent person" means one who is capable of identifying existing and predictable hazards in the surroundings or working conditions, which are unsanitary, hazardous, or dangerous to employees, and who has authorization to take prompt corrective measures to eliminate them.
Qualified Person
29 CFR 1926.32(l) states: "Qualified" means one who, by possession of a recognized degree, certificate, or professional standing, or who by extensive knowledge, training and experience, has successfully demonstrated his ability to solve or resolve problems relating to the subject matter, the work, or the project.

## Slide 28: Unattended
A condition in which the operator of a hoist is NOT at, or within 26 feet of, the operating control devices.
  OSHA 1910.179(n)(3)(x).

## Slide 29: “HOIST”
hoist (hoist) v. hoist·ed, hoist·ing, hoists
1. To raise or haul up with or as if with the help of a mechanical apparatus.
2. To raise to one's mouth in order to drink: hoist a few beers.

## Slide 30: Regardless of The Load You Hoist…

## Slide 31: …Or What You Hoist It With…

## Slide 32: …The Objective is to Hoist It Safely.
HOISTSAFE

## Slide 33: HOISTSAFE
 | H | 
 | O | 
 | I | 
 | S | 
 | T | 
 | S | 
 | A | 
 | F | 
 | E | 

## Slide 34: HOISTSAFE
How | H | heavy is the load?
 | O | 
 | I | 
 | S | 
 | T | 
 | S | 
 | A | 
 | F | 
 | E | 

## Slide 35: Determining Load Weight
Actual or calculated weight of object or materials being lifted
Include weight of rigging equipment and hardware
How HEAVY is the load?

## Slide 36: Determining Load Weight
Actual weight obtained from engineering data, shipping papers, catalogs.
Calculated weight based on common materials.
  Volume of object
  Weight of material
  Reduced for air (voids)
How HEAVY is the load?

## Slide 37: Determining Load Weight

## Slide 38: Worksheet Problem #1
800#
2,400#
4,800#
12,800#

## Slide 39: Worksheet Problem #1
4’ x 4’ x 16’ = 256 cubic feet
Wood weighs 50 pounds per cubic foot
256 c.f. x 50#/c.f. = 12,800#

## Slide 40: Worksheet Problem #2
1,415#
3,150#
9,900#
39,565#

## Slide 41: Worksheet Problem #2
Outside Diameter
  3.14 x (4 x 4 x 12) / 4
  150.72 Cu. Ft.
Inside Diameter
  3.14 x (3 x 3 x 12) / 4
  84.78 Cu. Ft.
Total Volume
  65.94 Cu. Ft.
66 cubic feet of concrete
150 pounds per cubic foot
66 x 150
TOTAL WEIGHT
  9,900 pounds

## Slide 42: Worksheet Problem #3
120#
140#
240#
480#

## Slide 43: Worksheet Problem #3
4’ x 3’ = 12 square feet
½” steel plate = 20 lbs/sq. ft.
12 s.f. x 20 lbs/sq. ft. = 240#

## Slide 44: Determining Load Weight
Known
  Data plate
  Engineering specifications
  Shipping papers
  “Tribal Knowledge”
Estimated
  Volume of object
  Density of materials
  Adjusted for voids (air)
How HEAVY is the load?

## Slide 45: HOISTSAFE
How | H | heavy is the load?
What are the | O | operating limitations of the crane and rigging?
 | I | 
 | S | 
 | T | 
 | S | 
 | A | 
 | F | 
 | E | 

## Slide 46: CRANE OPERATING CAPACITY
HOISTSAFE
What are the OPERATING LIMITATIONS of the crane and rigging?

## Slide 47: Crane Operating Capacity
What are the OPERATING LIMITATIONS of the crane and rigging?
Manufacturer's operating notes supplied with the machine contain important information concerning load handling capacities of cranes.
Mistakes in calculating capacity can cause accidents.
Several factors to be considered when calculating a cranes load capacity, including the following:

## Slide 48: Crane Operating Capacity
What are the OPERATING LIMITATIONS of the crane and rigging?
Load Radius: the horizontal distance between the center of the crane rotation to center of the load.
Boom length: including the jib, swing away extension or any other attachments that may increase length of the boom.
Quadrant of operation: the area of operation that the lift is being made in; note different quadrants usually have lower lifting capacities.

## Slide 49: Crane Operating Capacity
What are the OPERATING LIMITATIONS of the crane and rigging?
Boom angle: the angle formed between the horizontal plane of rotation and center line of the boom.
Weight of any attachments: jib, lattice extension or auxiliary boom point.
Weight of handling devices: ball, block, and/or any necessary rigging.

## Slide 50
LOAD RADIUS (FT) | BOOM LENGTH 35’ |  |  | BOOM LENGTH 50’ |  |  | BOOM LENGTH 65’ |  |  | LOAD RADIUS (FT)
 | BOOM ANGLE | OVER FRONT (LBS) | 360° (LBS) | BOOM ANGLE | OVER FRONT (LBS) | 360° (LBS) | BOOM ANGLE | OVER FRONT (LBS) | 360° (LBS) | 
10 | 66.7 | 110,000 | 110,000 | 73.9 | 60,100 | 60,100 |  |  |  | 10
12 | 63.1 | 96,700 | 93,700 | 71.5 | 60,100 | 60,100 |  |  |  | 12
15 | 57.5 | 75,200 | 73,100 | 69.7 | 60,100 | 60,100 | 73.2 | 58,800 | 58,800 | 15
20 | 47.1 | 53,600 | 52,300 | 61.5 | 54,900 | 53,600 | 68.5 | 52,200 | 52,200 | 20
25 | 34.5 | 40,700 | 39,700 | 54.8 | 42,000 | 41,100 | 63.7 | 42,700 | 41,700 | 25
30 | 14.8 | 31,900 | 31,200 | 47.4 | 33,400 | 32,700 | 58.6 | 34,100 | 33,400 | 30
35 |  |  |  | 39.0 | 27,300 | 26,700 | 53.3 | 28,000 | 27,400 | 35
40 |  |  |  | 28.8 | 22,000 | 21,000 | 47.6 | 22,700 | 21,700 | 40
45 |  |  |  | 12.4 | 17,400 | 16,500 | 41.3 | 18,300 | 17,400 | 45
50 |  |  |  |  |  |  | 34.1 | 14,900 | 14,200 | 50
55 |  |  |  |  |  |  | 25.2 | 12,300 | 11,700 | 55
60 |  |  |  |  |  |  | 10.9 | 10,100 | 9,600 | 60

## Slide 51: Sling Capacity
HOISTSAFE
What are the OPERATING LIMITATIONS of the crane and rigging?

## Slide 52: Sling Capacity
Load bearing material
  Alloy chain
  Wire rope
  Synthetic
  Metal mesh
Upper and Lower End Attachments
What are the OPERATING LIMITATIONS of the crane and rigging?

## Slide 53: Alloy Chain slings
HOISTSAFE
What are the OPERATING LIMITATIONS of the crane and rigging?

## Slide 54: Alloy Chain Slings
Advantages
Flexible
Impact resistant
Easy to inspect
Can be used at relatively high temperatures
Completely repairable
Minimum elongation
Corrosion resistant
Durable
Disadvantages
Heavy
Moderate initial cost
What are the OPERATING LIMITATIONS of the crane and rigging?

## Slide 55: NACM WELDED STEEL CHAIN SPECIFICATIONS
Grade 30 Proof Coil Chain
  General purpose, carbon steel chain. Used in a wide range of applications.
  Not to be used in overhead lifting.
What are the OPERATING LIMITATIONS of the crane and rigging?

## Slide 56: NACM WELDED STEEL CHAIN SPECIFICATIONS
Grade 43 High Test Chain
  A carbon steel chain widely used in industry, construction, agricultural and lumbering operations.
  Not to be used in overhead lifting.
What are the OPERATING LIMITATIONS of the crane and rigging?

## Slide 57: NACM WELDED STEEL CHAIN SPECIFICATIONS
Grade 70 Transport Chain
  A high quality, high strength carbon steel chain used for load securing.
  Not to be used in overhead lifting.
What are the OPERATING LIMITATIONS of the crane and rigging?

## Slide 58: NACM WELDED STEEL CHAIN SPECIFICATIONS
Grade 80 Alloy Chain
  Premium quality, high strength alloy chain, heat treated, used in a variety of sling and tie down applications.
  For overhead lifting applications, only Alloy Chain should be used.
What are the OPERATING LIMITATIONS of the crane and rigging?

## Slide 59: NACM WELDED STEEL CHAIN SPECIFICATIONS
Grade 100 Alloy Chain
  Premium quality, highest strength alloy chain, heat treated, used in a variety of sling and tie down applications.
  For overhead lifting applications, only Alloy Chain should be used.
What are the OPERATING LIMITATIONS of the crane and rigging?

## Slide 60: Elongation
Elongation shall not be less than:
  20% for Grades 80 and 100;
  15% for Grades 30, 43, 70, and Stainless;
  10% for Machine, Coil, and Passing Link chain.
What are the OPERATING LIMITATIONS of the crane and rigging?

## Slide 61: Working Load Limit
 | Working Load Limit (lbs) |  |  |  |  | 
Size | Proof Coil Grade 30 | High Test Grade 43 | Transport Grade 70 | Alloy Grade 80 | Alloy Grade 100 | Alloy Grade 120
1/4 | 1,300 | 2,600 | 3,150 |  |  | 
9/32 |  |  |  | 3,500 | 4,300 | 5,200
5/16 | 1,900 | 3,900 | 4,700 | 4,500 | 5,700 | 
3/8 | 2,650 | 5,400 | 6,600 | 7,100 | 8,800 | 10,600
1/2 | 4,500 | 9,200 | 11,300 | 12,000 | 15,000 | 17,900
5/8 | 6,900 | 13,000 | 15,800 | 18,100 | 22,600 | 
3/4 |  |  |  | 28,300 |  | 
7/8 |  |  |  | 34,200 |  | 
1 |  |  |  | 47,700 |  | 
1-1/4 |  |  |  | 72,300 |  | 

## Slide 62: Ambient Conditions
High temperatures can significantly reduce the W.L.L. of slings.
Extreme temperatures can cause permanent damage.
  Foundries
  Arc welding
What are the OPERATING LIMITATIONS of the crane and rigging?

## Slide 63: Reduction of Working Load Limit
Chains should not be used outside of the -40°F to 400°F (-40 °C to 204 °C) temperature range without consulting the chain manufacturer.
The specific working load limit reductions for Grade 80 and Grade 100 chains used at and after exposure to elevated temperatures have been established and are shown in Table XII.
What are the OPERATING LIMITATIONS of the crane and rigging?

## Slide 64: Reduction Of Working Load Limit
Temperature |  | Grade Of Chain |  |  | 
°F | °C | Grade 80 |  | Grade 100 | 
 |  | While At Temperature | After Exposure | While At Temperature | After Exposure
<400 | <204 | None | None | None | None
400 | 204 | 10% | None | 15% | None
500 | 260 | 15% | None | 25% | 5%
600 | 316 | 20% | 5% | 30% | 15%
700 | 371 | 30% | 10% | 40% | 20%
800 | 427 | 40% | 15% | 50% | 25%
900 | 482 | 50% | 20% | 60% | 30%
1,000 | 538 | 60% | 25% | 70% | 35%
>1,000 | >538 | OSHA 1910.184 requires all slings exposed to temperatures over 1000° F to be removed from service |  |  | 

## Slide 65: Wire Rope SLINGS
HOISTSAFE
What are the OPERATING LIMITATIONS of the crane and rigging?

## Slide 66: Wire Rope Slings
Advantages
Low initial cost
Lighter weight than alloy chain
Disadvantages
Low strength to weight ratio
Difficult to inspect
Easily kinked
Internal corrosion
Not repairable
What are the OPERATING LIMITATIONS of the crane and rigging?

## Slide 67: Wire Rope Slings
Mechanical Splice Slings – Single Part Body – IPS – 6 x 19 IWRC RATED CAPACITY (lbs.) |  |  |  |  | 
 |  |  | Basket Hitch – Sling Angle |  | 
Size (in.) | Vertical | Choker | 90° | 60° | 45°
1 / 4 | 1,120 | 820 | 2,200 | 1,940 | 1,580
3 / 8 | 2,400 | 1,840 | 4,800 | 4,200 | 3,400
1 / 2 | 4,400 | 3,200 | 8,800 | 7,600 | 6,200
5 / 8 | 6,800 | 5,000 | 13,600 | 11,800 | 9,600
3 / 4 | 9,800 | 7,200 | 19,600 | 17,000 | 13,800
7 / 8 | 13,200 | 9,600 | 26,000 | 22,000 | 18,600
1 | 17,000 | 12,600 | 34,000 | 30,000 | 24,000
1 – 1 / 8 | 20,000 | 15,800 | 40,000 | 34,000 | 28,000
 |  |  | D/d ratio is 20 or greater |  | 

## Slide 68: Wire Rope Slings
What are the OPERATING LIMITATIONS of the crane and rigging?

## Slide 69: Metal Mesh SLINGS
HOISTSAFE
What are the OPERATING LIMITATIONS of the crane and rigging?

## Slide 70: Metal Mesh Slings
Advantages
Flexibility
Wide bearing surface
Resists abrasion and cutting
Resists corrosion
Disadvantages
Subject to crushing
Any broken wire is cause for removal from service
What are the OPERATING LIMITATIONS of the crane and rigging?

## Slide 71: Synthetic SLINGS
HOISTSAFE
What are the OPERATING LIMITATIONS of the crane and rigging?

## Slide 72: Synthetic Slings
Advantages
Light weight
Easy to rig
Low initial cost
Reduced load damage
Disadvantages
Low heat resistance
  194° F.
Subject to cuts and abrasion
Subject to chemicals and UV
Cannot be repaired
What are the OPERATING LIMITATIONS of the crane and rigging?

## Slide 73: Synthetic Clings
Flat / Tubular Slings
Round Slings
What are the OPERATING LIMITATIONS of the crane and rigging?

## Slide 74: Polyester Round Slings
Width (In.) | Color | Rated Capacity (Lbs.) |  | 
 |  | Vertical | Choker | Basket
2 | Purple | 3,000 | 2,400 | 6,000
 | Black | 4,500 | 3,600 | 9,000
 | Green | 6,000 | 4,800 | 12,000
 | Yellow | 9,000 | 7,200 | 18,000
3 | Gray | 12,000 | 9,600 | 24,000
 | Red | 14,000 | 11,200 | 28,000
 | Brown | 17,000 | 13,600 | 34,000
 | Blue | 22,000 | 17,600 | 44,000
4 | Orange | 26,000 | 20,800 | 52,000
 |  | 32,000 | 25,600 | 64,000
5 |  | 50,000 | 40,000 | 100,000
 |  | 60,000 | 48,000 | 120,000

## Slide 75: Number of Attachment Points
Double leg slings share the load equally*
Triple leg slings have 50% more capacity than double leg slings.
Quad leg slings rely on the fourth leg for stability only, not additional lift capacity.
What are the OPERATING LIMITATIONS of the crane and rigging?

## Slide 76: Operating Limitations
Crane Capacity Charts
  Mobile Crane
    Boom angle
    Boom extension
  Overhead Crane
  Static versus Dynamic loads
Slings and Hardware
  Vertical capacity
  Basket capacity
  Choker capacity
  Bridle capacity
What are the OPERATING LIMITATIONS of the crane and rigging?

## Slide 77: HOISTSAFE
How | H | heavy is the load?
What are the | O | operating limitations of the crane and rigging?
When was the last | I | inspection performed?
 | S | 
 | T | 
 | S | 
 | A | 
 | F | 
 | E | 

## Slide 78: Sling Inspection
HOISTSAFE
When was the last INSPECTION performed?

## Slide 79: Every sling inspection must be documented.
True
False

## Slide 80: OSHA 1910.184 ASME B30.9
Reasons
  Ensure safe equipment
  Gain knowledge and experience:
    Nature of lifts being made
    Sling usage
    Operator competence
Inspections
  Daily / Periodic before use (NO records)
  Minimum annual with records
  Frequently, as warranted
Record Keeping
  Most recent report
  Test certificates
When was the last INSPECTION performed?

## Slide 81: Periodic inspection of slings should be performed by a competent person.
True
False

## Slide 82: Daily / Period Inspection
A thorough periodic inspection of slings shall be performed by a competent person designated by the employer and shall include a thorough inspection for:
Wear
Deformation
Elongation
Sharp traverse nicks and gouges in chain
Cuts
Corrosion
Heat damage
Hardware
  Latches for proper seating, operation and distortion
  Hooks for wear and distortion
When was the last INSPECTION performed?

## Slide 83: HOISTSAFE
How | H | heavy is the load?
What are the | O | operating limitations of the crane and rigging?
When was the last | I | inspection performed?
How will | S | sling angles affect lifting capacity?
 | T | 
 | S | 
 | A | 
 | F | 
 | E | 

## Slide 84: Sling Angle

## Slide 85: A 24-can case of beer weighs…
10 pounds
15 pounds
20 pounds
25 pounds

## Slide 86: Beer Facts
One can of beer weighs 13.1 ounces
  13.1 oz. x 24 cans = 314.4 oz.
The cardboard box weighs 7 ounces
  314.4 + 7 = 321.4 oz.
321.4 oz. ÷ 16 oz. per pound
20 pounds

## Slide 87: How much does it weigh?
How will SLING ANGLES affect lifting capacity?

## Slide 88: How heavy does it feel?
How will SLING ANGLES affect lifting capacity?

## Slide 89: Sling Angle Factor
SLING ANGLE CHART | 
Angle from Horizontal [A] | S.A.F. [L ÷ H]
90° | 1.000
60° | 1.155
45° | 1.415
30° | 2.000
A

## Slide 90: Sling Angle Factor

## Slide 91: Worksheet Problem #4
1,700#
2,268#
2,266#
567#

## Slide 92: Worksheet Problem #4
How many legs will actually carry the load?
  Three

## Slide 93: Worksheet Problem #4
What is the share of the load?
  1,133.3333333333#

## Slide 94: Worksheet Problem #4
What is the load factor?
  3’ ÷ 1.5’ = 2.0

## Slide 95: Worksheet Problem #4
What is the tension in each sling leg?
  2.0 x 1,133# = 2,266#
  2.0 x 1,134# = 2,268#

## Slide 96: Worksheet Problem #5
1,746#
5,856#
5,888#
6,400#

## Slide 97: Worksheet Problem #5
What is the share of the load?
  6,400# ÷ 2 = 3,200#

## Slide 98: Worksheet Problem #5
What is the load factor?
  5.5 ÷ 3 = 1.83333333333333
  1.83
  1.84
  2.00

## Slide 99: Worksheet Problem #5
What is the tension in each sling leg?
  3,200# x 1.833333333 = 5,866.6666666667#
  5,856#
  5,888#
  6,400#

## Slide 100: Worksheet Problem #5
What other factors might affect sling capacity?
  Wet environment for synthetic slings
  Dynamic loading as object enters and leaves water

## Slide 101: Grade 80 Alloy Chain Slings
Single |  | 
Chain Trade Size | Chain Size | Working Load Limit (lbs)
9/32” | .279 | 3,500
3/8” | .404 | 7,100
½” | .529 | 12,000
5/8” | .625 | 18,100
¾” | .801 | 28,300
7/8” | .881 | 34,200
1” | 1.000 | 47,700
1-1/4” | 1.250 | 72,300
How will SLING ANGLES affect lifting capacity?

## Slide 102: Grade 80 Alloy Chain Slings
Double |  | 90° | 60° | 45° | 30°
Chain Trade Size | Chain Size | Working Load Limit (lbs) |  |  | 
9/32” | .279 | 7,000 | 6,100 | 4,900 | 3,500
3/8” | .404 | 14,200 | 12,300 | 10,000 | 7,100
½” | .529 | 24,000 | 20,800 | 17,000 | 12,000
5/8” | .625 | 36,200 | 31,300 | 25,600 | 18,100
¾” | .801 | 56,600 | 49,000 | 40,000 | 28,300
7/8” | .881 | 68,400 | 59,200 | 48,400 | 34,200
1” | 1.000 | 95,400 | 82,600 | 67,400 | 47,700
1-1/4” | 1.250 | 144,600 | 125,200 | 102,200 | 72,300
How will SLING ANGLES affect lifting capacity?

## Slide 103: Grade 80 Alloy Chain Slings
T & Q |  | 90° | 60° | 45° | 30°
Chain Trade Size | Chain Size | Working Load Limit (lbs) |  |  | 
9/32” | .279 | 10,500 | 9,100 | 7,400 | 5,200
3/8” | .404 | 21,300 | 18,400 | 15,100 | 10,600
½” | .529 | 36,000 | 31,200 | 25,500 | 18,000
5/8” | .625 | 54,300 | 47,000 | 38,400 | 27,100
¾” | .801 | 84,900 | 73,500 | 60,000 | 42,200
7/8” | .881 | 102,600 | 88,900 | 72,500 | 51,300
1” | 1.000 | 143,100 | 123,900 | 101,200 | 71,500
1-1/4” | 1.250 | 216,900 | 187,800 | 153,400 | 108,400
How will SLING ANGLES affect lifting capacity?

## Slide 104: Wire Rope Slings
Mechanical Splice Slings – Single Part Body – IPS – 6 x 19 IWRC RATED CAPACITY (lbs.) |  |  |  |  | 
 |  |  | Basket Hitch – Sling Angle |  | 
Size (in.) | Vertical | Choker | 90° | 60° | 45°
1 / 4 | 1,120 | 820 | 2,200 | 1,940 | 1,580
3 / 8 | 2,400 | 1,840 | 4,800 | 4,200 | 3,400
1 / 2 | 4,400 | 3,200 | 8,800 | 7,600 | 6,200
5 / 8 | 6,800 | 5,000 | 13,600 | 11,800 | 9,600
3 / 4 | 9,800 | 7,200 | 19,600 | 17,000 | 13,800
7 / 8 | 13,200 | 9,600 | 26,000 | 22,000 | 18,600
1 | 17,000 | 12,600 | 34,000 | 30,000 | 24,000
1 – 1 / 8 | 20,000 | 15,800 | 40,000 | 34,000 | 28,000
 |  |  | D/d ratio is 20 or greater |  | 
How will SLING ANGLES affect lifting capacity?

## Slide 105: Sling Angle – Unequal Legs

## Slide 106: Sling Angle – Unequal Legs
How will SLING ANGLES affect lifting capacity?
D1 = 3’ D2 = 7’
H = 4’
S1 = 5’
S2 = 8’
L = 1,000#

## Slide 107: Sling 1
Tension = Load x D2 x S1/(H(D1 + D2))
Tension = 1,000 x 7 x 5/(4(3+7))
Tension = 1,000 x 7 x 5/40
Tension = 1,000 x 7 x 0.125
Tension = 875#

## Slide 108: Sling 2
Tension = Load x D1 x S2/(H(D1 + D2))
Tension = 1,000 x 3 x 8/(4(3+7))
Tension = 1,000 x 3 x 8/40
Tension = 1,000 x 3 x 0.2
Tension = 600#

## Slide 109: Sling Angle – Unequal Legs
How will SLING ANGLES affect lifting capacity?
S1 = 875#
S2 = 600#
L = 1,000#

## Slide 110: Sling Angle – Spreader Beam
Distributes load evenly without excessive sling angles
Requires greater headroom clearance
How will SLING ANGLES affect lifting capacity?

## Slide 111: Vertical Basket Hitch
Two times the single leg capacity
Legs must be vertical to within 5 degrees
D/d must be greater than 20/1
How will SLING ANGLES affect lifting capacity?
D
d

## Slide 112: Double Wrap Basket Hitch
Excellent load control for loose materials and good grip on smooth surfaces.
Twice the single leg capacity.
Sling wrap must be lay side by side
Do not overlap at bottom of load
Adjust sling as slack is taken up
How will SLING ANGLES affect lifting capacity?

## Slide 113: Choker Hitch
75-80% OF SINGLE LEG CAPACITY
ANGLE OF CHOKE MUST BE GREATER THAN 120 DEGREES
How will SLING ANGLES affect lifting capacity?

## Slide 114: Double Wrap Choker Hitches
EXCELLENT LOAD CONTROL FOR LOOSE MATERIALS AND GRIP ON SMOOTH SURFACES
75-80% OF SINGLE LEG CAPACITY
ANGLE OF CHOKE MUST BE GREATER THAN 120 DEGREES
SLING WRAP MUST LAY SIDE BY SIDE
DO NOT OVERLAP AT BOTTOM OF LOAD
How will SLING ANGLES affect lifting capacity?

## Slide 115: Sling Angles – Edge Protection
When edges are sharp or abrasive
  Sling damage may occur
When sling angle become shallow.
  Lateral loading may crush object being lifted.
How will SLING ANGLES affect lifting capacity?

## Slide 116: Sling Angles
Sling tension
  Loads tend to hang vertically
  Forcing load points away from vertical requires force
  Reaction to the force increases sling tension
Crush Force
  The result of forcing load points away from vertical
Cribbing
  Protects the sling from being damaged
  Protects the load from being crushed
How will SLING ANGLES affect lifting capacity?

## Slide 117: HOISTSAFE
How | H | heavy is the load?
What are the | O | operating limitations of the crane and rigging?
When was the last | I | inspection performed?
How will | S | sling angles affect lifting capacity?
Have you performed a | T | test lift to check stability?
 | S | 
 | A | 
 | F | 
 | E | 

## Slide 118: Load Stability
HOISTSAFE
Have you performed a TEST LIFT to verify stability?

## Slide 119: Load Stability
Capture the Center-of-Gravity
  When suspended an object will always center itself under the lift point
  Center the lift above the center of gravity, not the physical center of the object
  Calculating the C.G.
Have you performed a TEST LIFT to verify stability?

## Slide 120: Center of Gravity
Have you performed a TEST LIFT to verify stability?

## Slide 121: Center of Gravity
Have you performed a TEST LIFT to verify stability?

## Slide 122: HOISTSAFE
How | H | heavy is the load?
What are the | O | operating limitations of the crane and rigging?
When was the last | I | inspection performed?
How will | S | sling angles affect lifting capacity?
Have you performed a | T | test lift to check stability?
Move the load with | S | smooth and steady actions
 | A | 
 | F | 
 | E | 

## Slide 123: Safe Hoist and crane Operations
HOISTSAFE
Move the load with SMOOTH AND STEADY actions.

## Slide 124: Safe Hoist and Crane Operations
General
  Make certain that multiple-part lines are not twisted around each other.
  Be sure that hoist rope or chain is properly seated in sheaves or pocketwheels.
  Make certain that the load will not contact any obstructions.
  Avoid swinging the load or load hook while traveling.
  Avoid sudden acceleration and deceleration of the load.
Move the load with SMOOTH AND STEADY actions.

## Slide 125: Safe Hoist and Crane Operations
General
  Avoid severe contact between the trolley and trolley stops on the tracks, and between a crane and crane stops on railways.
  When winds become dangerous high during an outdoor job, discontinue use of the equipment and anchor it as recommended.
Move the load with SMOOTH AND STEADY actions.

## Slide 126: Safe Hoist and Crane Operations
General
  If power is interrupted during operation of a crane or hoist, place all controls in the “OFF” position.
  If more than one hoist or crane must be used to lift or move a load, ONE person should be assigned responsibility for the operation.
Move the load with SMOOTH AND STEADY actions.

## Slide 127: Safe Hoist and Crane Operations
Special Heavy Lifts
  Lifts in excess of the rated capacity
  Each heavy lift must be analyzed and authorized by a qualified person
  ONLY applies to the specific lift
    Does NOT authorize any heavy lifts in everyday operations
Move the load with SMOOTH AND STEADY actions.

## Slide 128: Safe Hoist and Crane Operations
Pulling a Load
  Use of hoists and cranes for pulling a load is NOT recommended.
  If necessary use a pulley (snatch) block to re-direct force to the load.
  Avoid ‘side pull’ on the hoist.
  Use second hoist anchored to a structural member to achieve load pulls
  Consult supervisor before any load pulling operations
Move the load with SMOOTH AND STEADY actions.

## Slide 129: Safe Hoist and Crane Operations
Turning a Load
  Visualize the load and its center of gravity
  Visualize sling positions while turning
  Determine if blocks or supports will be required
  Determine how load will be controlled
    Tagline
    Two-hook turn
Move the load with SMOOTH AND STEADY actions.

## Slide 130: Safe Hoist and Crane Operations
Smooth, steady application of lifting force
  Allows hoist and rigging to adjust to change
  Minimizes spin
  Reduces wear on wire and synthetic rope
NO shock loading
  Especially with wire rope slings
Move the load with SMOOTH AND STEADY actions.

## Slide 131: Standard hand signals
HOISTSAFE
Move the load with SMOOTH AND STEADY actions.

## Slide 132: Standard Hand Signals
Move the load with SMOOTH AND STEADY actions.

## Slide 133: HOISTSAFE
How | H | heavy is the load?
What are the | O | operating limitations of the crane and rigging?
When was the last | I | inspection performed?
How will | S | sling angles affect lifting capacity?
Have you performed a | T | test lift to check stability?
Move the load with | S | smooth and steady actions
Is the | A | area clear of personnel and obstructions?
 | F | 
 | E | 

## Slide 134: Area Clear
Personnel
  Barriers and warning signs
  May distract crane operator
  Security personnel
Vehicles and equipment
  Block visibility
Is the AREA CLEAR of personnel and obstructions?

## Slide 135: HOISTSAFE
How | H | heavy is the load?
What are the | O | operating limitations of the crane and rigging?
When was the last | I | inspection performed?
How will | S | sling angles affect lifting capacity?
Have you performed a | T | test lift to check stability?
Move the load with | S | smooth and steady actions
Is the | A | area clear of personnel and obstructions?
Can the load be | F | Flown and landed safely?
 | E | 

## Slide 136: Flying the Load
Is there a clear, unobstructed path from lift point to landing?
Do NOT fly the load over people.
Maintain clearance from objects such as buildings, vehicles and utilities.
Can the load be FLOWN AND LANDED safely?

## Slide 137: Flying the Load
Can the load be FLOWN AND LANDED safely?

## Slide 138: Flying the Load
Utility lines
  Clearly identified
  Shielding
  Maintain minimum clearances
Voltage | Distance from Power Lines
≤ 50kV | 10 feet
200 kV | 15 feet
350 kV | 20 feet
500 kV | 25 feet
650 kV | 30 feet
800 kV | 35 feet
Construction Safety Council | 
Can the load be FLOWN AND LANDED safely?

## Slide 139: Flying the Load
Swing and Travel
  Use smooth, steady motions to fly the load.
  Keep the load under control.
  Avoid dynamic loading or load shifting.
Can the load be FLOWN AND LANDED safely?

## Slide 140: Landing the Load
Plan where the load will be landed before lifting.
  Consider the weight, type, and shape of load.
Land the load on a firm, flat surface.
Can the load be FLOWN AND LANDED safely?

## Slide 141: Landing the Load
Land load on blocks / cribbing to allow removal of slings.
  NEVER land a load directly on the slings.
Chock cylindrical loads to prevent rolling.
Slowly relieve tension on hoist and rigging.
Can the load be FLOWN AND LANDED safely?

## Slide 142: HOISTSAFE
How | H | heavy is the load?
What are the | O | operating limitations of the crane and rigging?
When was the last | I | inspection performed?
How will | S | sling angles affect lifting capacity?
Have you performed a | T | test lift to check stability?
Move the load with | S | smooth and steady actions
Is the | A | area clear of personnel and obstructions?
Can the load be | F | flown and landed safely?
How will the | E | environment affect the safety of the lift?

## Slide 143: Environmental Considerations
Weather
Terrain
Chemical Conditions and Exposure
How will the ENVIRONMENT affect the safety of the lift?

## Slide 144: Tag lines are only required when winds exceed 20 mph
True
False

## Slide 145: Weather
Wind
  Tag lines shall be used unless their use creates an unsafe condition [OSHA 1926.550(g)(6)(iii)]
How will the ENVIRONMENT affect the safety of the lift?

## Slide 146: Rigging is affected at temperatures…
Below -40° F
Below 32° F
Above 190° F
Above 400° F

## Slide 147: Weather
Wind
Temperature
  Chain and wire rope affected below -40° F
  Synthetic affected above 190° F
  Wire rope affected above 300° F
  Chain affected above 400° F
How will the ENVIRONMENT affect the safety of the lift?

## Slide 148: Weather
Wind
Temperature
Precipitation
How will the ENVIRONMENT affect the safety of the lift?

## Slide 149: Weather
Wind
Temperature
Precipitation
Visibility
How will the ENVIRONMENT affect the safety of the lift?

## Slide 150: Terrain
Level
Dry
Stable
  Wet / Mud
  Frozen
How will the ENVIRONMENT affect the safety of the lift?

## Slide 151: Chemical Conditions and Exposure
Corrosives
  Attack all metal components
  Attack certain types of synthetic components
How will the ENVIRONMENT affect the safety of the lift?

## Slide 152: Corrosives
NYLON
Nylon has excellent resistance to most substances.
Nylon has excellent resistance to hydrocarbons (such as gasoline, kerosene and diesel fuel), oils, cleaning solutions and alkalis.
  It is however attacked by oxidizing agents, organic acids, mineral acids and aromatic alcohols.
POLYESTER
Polyester has excellent resistance to most substances.
It is resistant to acids, oxidizers such as hydrogen peroxide and most solvents.
Polyester has excellent resistance to hydrocarbon fuels, oils and lubricants.
  It is however attacked by strong alkalis
How will the ENVIRONMENT affect the safety of the lift?

## Slide 153: Safe Rigging Practices
Rigging Fundamentals

## Slide 154: The Thought Process of Rigging
What is to be done with the load?
What tools are needed to perform the assigned task?
Is the capacity of the tools adequate to handle the loads and forces involved in lifting and moving?
How can the hookup be made?
What will happen when the load is lifted?

## Slide 155: Safe Rigging Practices
Whenever possible, avoid sharp, inefficient sling angles by using longer slings or a spreader beam.
Do not pull slings from under a load when the load is resting on the sling.
Do not drag slings over sharp objects or abrasive surfaces.
Do not leave slings lying where heavy loads may be set down on top of them, or where vehicles may drive over them.

## Slide 156: Safe Rigging Practices
Slings should be stored in an assigned area.
  The storage should be such that the slings will not be subject to kinking or other mechanical damage, corrosive atmosphere, or excessive temperature.
Damaged slings should always be repaired before they are placed in the assigned storage area.
Do NOT make temporary repairs of slings with miscellaneous or makeshift parts.
Fiber-rope slings should not be made from ropes less than ½ inch in diameter.

## Slide 157: Safe Rigging Practices
Do not use metal-mesh slings in which the spirals are locked or do not move freely.
Do NOT hammer a metal-mesh sling to straighten a spiral or cross rod, or to force a spiral into position.
If metal-mesh slings are used in pairs, they should be attached to a spreader beam.

## Slide 158: Who is responsible for safe rigging?
OSHA
ANSI
Competent person
Everyone associated with the movement of the load

## Slide 159
Make Every Day a Safe Workday!