## Slide 1: Electrical jeopardy
Electrical Jeopardy
This material was produced under grant SH31244SH7 from the Occupational Safety and Health Administration, U.S. Department of Labor. It does not necessarily reflect the views or policies of the U.S. Department of Labor, nor does mention of trade names, commercial products, or organizations imply endorsement by the U.S. Government.

## Slide 2: Jeopardy categories

## Slide 3: Flow of electrical energy.

## Slide 4: What is current

## Slide 5: Material through which current moves easily

## Slide 6: What is a conductor

## Slide 7: Glass, rubber, plastic, dry wood, paper, ceramics, and air

## Slide 8: What are insulators

## Slide 9: Inversely proportional to current; opposition to flow

## Slide 10: What is resistance

## Slide 11: A fatal electric shock

## Slide 12: What is electrocution

## Slide 13: Accidentally becoming part of this can cause injury or death

## Slide 14: What is an energized electrical circuit

## Slide 15: The threshold for ventricular fibrillation

## Slide 16: What is 100 milliamps (mA) of current

## Slide 17: Three factors that affect the severity of electrical shock

## Slide 18: What are: path through body; amount of current; length of time

## Slide 19: This is said to “push” current through a conductor

## Slide 20: What is Voltage

## Slide 21: Measures strength of current flow

## Slide 22: What is Amperage

## Slide 23: These protect electrical systems and equipment from overcurrent

## Slide 24: What are circuit breakers and fuses

## Slide 25: Luminous electrical discharge through the air

## Slide 26: What is arcing

## Slide 27: This hazard is the primary source of electrocutions

## Slide 28: What are overhead power lines

## Slide 29: The minimum safe distance to maintain away from power lines ≤ 50,000 V

## Slide 30: What is 10 feet

## Slide 31: The only ladders you may use near energized circuits

## Slide 32: What are non-conductive (fiberglass or wood)

## Slide 33: When this shield is worn, frayed or cut, workers are at high risk for shock

## Slide 34: What is the insulation around an energized conductor

## Slide 35: A conductor added to circuits to create a low resistive path to neutral or earth

## Slide 36: What is a ground wire

## Slide 37: A safety device required by OSHA on construction site circuits

## Slide 38: What is a GFCI (ground fault circuit interrupter)

## Slide 39: A ground conductor loses its connectivity if this is missing from a plug

## Slide 40: What is the ground prong

## Slide 41: “S, ST, SO, STO” for example

## Slide 42: What are extension cord usage rating codes