## Slide 1: EXCAVATION AND TRENCHING
OSHA - Susan Harwood Training Grant

## Slide 2: Welcome
Please sign the attendance sheet
Take one handout
Answer the pre-test

## Slide 3: location
Emergency Exits
Emergency Stairs
Location of restrooms
Location of water fountains

## Slide 4: Disclaimer
This material was produced under grant number SH-16582-SH7 (2007) from the Occupational Safety and Health Administration, U.S. Department of Labor. It does not necessarily reflect the views or policies of the U. S. Department of Labor, nor does mention of trade names, commercial products, or organizations imply endorsement by the U. S. Government.
Revisions were made to this material under grant number SH-05120-SH9 from the Occupational Safety and Health Administration, U.S. Department of Labor.

## Slide 5: Agenda
Welcome
Introduction to OSHA
Worker’s rights
Introduction to Trenching and Excavation Hazards
  What is trenching?
  Preventing excavation hazard
Common Trenching and Excavation Hazards
Soil Classifications
Exercises
Certificates

## Slide 6: Introduction to osha
Overview of anti-retaliation provisions, employee rights, employer responsibilities, whistleblower laws, and OSHA’s complaint investigation procedures

## Slide 7: Why is OSHA Important to You?
OSHA began because, until 1970, there were no national laws for safety and health hazards.
On average, 14 workers die every day from job injuries
Worker deaths in America are down–on average, from about 38 worker deaths a day in 1970 to 14 a day in 2017
WORKER FATALITIES
5,147 workers died at the job in 2017, 971(20.7%) worked in construction
Excavation — an average of 19 death per year, from a low of 10 death in 2014 to a high of 33 death in 2016
(Source: BLS 2018)

## Slide 8: Discussion Questions
When, during your work experience, did you first hear about OSHA?
What did you think about OSHA then?
What do you think OSHA’s job is?

## Slide 9: History of OSHA
OSHA stands for the Occupational Safety and Health Administration, an agency of the U.S. Department of Labor
OSHA’s responsibility is worker safety and health protection
On December 29, 1970, President Nixon signed the OSH Act
This Act created OSHA, the agency, which formally came into being on April 28, 1971

## Slide 10: OSHA’s Mission
To save lives
To prevent injuries
To protect America’s workers

## Slide 11: Strategies to Reduce Injuries and Deaths
Strong, fair, and effective enforcement.
Outreach, education, and compliance assistance.
Partnerships and other cooperative programs.

## Slide 12: HCS PICTOGRAMS AND HAZARDS
Labels for hazardous substances in your workplace

## Slide 13: OSHA Inspections
The OSH Act authorizes OSHA compliance safety and health officers (CSHOs) to conduct workplace inspections at reasonable times.
OSHA conducts inspections without advance notice, except in rare circumstances (e.g. Imminent Danger)
In fact, anyone who tells an employer about an OSHA inspection in advance can receive fines and a jail term.

## Slide 14: Inspections Process
A typical OSHA on-site inspection includes four stages:
Presentation of inspector credentials.
An opening conference.
An inspection walk-around.
A closing conference.

## Slide 15: OSHA’s Inspection Priorities
Priority | Category of Inspection
1st | Imminent Danger: Reasonable certainty an immediate danger exists
2nd | Fatality/Catastrophe: Reported to OSHA; inspected ASAP
3rd | Complaints/Referrals: Worker or worker representative can file a complaint about a safety or health hazard
4th | Programmed Inspections: Cover industries and employers with high injury and illness rates, specific hazards, or other exposures.

## Slide 16: OSHA’s Complaint Investigations
OSHA evaluates each complaint to determine how it can be handled best--an off-site investigation or an on-site inspection
Before beginning an inspection, OSHA staff must be able to determine from the complaint that there are reasonable grounds to believe that a violation of an OSHA standard or a safety or health hazard exists.
If OSHA has information indicating the employer is aware of the hazard and is correcting it, the agency may not conduct an inspection after obtaining the necessary documentation from the employer.

## Slide 17: CONT.
Employee may file a complain with OSHA under Section 11(c) if your employer retaliates against you by taking unfavorable personnel action because you engaged in protected activity relating to workplace safety and health.
OSHA requires that complaints must be filed within 30 days after the alleged retaliation.

## Slide 18: Rights as a Whistleblower
Your employer may be found to have retaliated against you if your protected activity was a contributing or motivating factor in its decision to take unfavorable personnel action against you. Such actions may include:
  Firing or laying off
  Blacklisting
  Denying overtime or promotion
  Disciplining
  Denying benefits
  Failing to hire or rehire
  Intimidation
  Reassignment affecting promotion prospects
  Reducing pay or hour

## Slide 19: Questions about OSHA?

## Slide 20: DEFINITIONS
Excavation
Any man-made cavity or depression in the earth’s surface (including its walls, floor and lip) formed by earth removal. For rescue purposes an excavation is wider than it is deep.

## Slide 21: definitions
Trench
A narrow excavation which is deeper than it is wide, with a maximum width of fifteen (15) feet measured at the floor (bottom).

## Slide 22: Excavations Overview / Main Points
Excavation laws, regulations, standards
Soil classification
Soil testing
Competent person responsibilities
Hazards associated with trenches
Protective systems

## Slide 23: Tragic Facts
Excavating is recognized as one of the most hazardous construction operations
  97 Workers were killed on Excavation/Trenching jobs from 2013-2017.
  From a low of 10 deaths in 2014 to a high of 33 in 2016.
  Cave-ins are more likely than other excavation related accidents to result in worker fatalities.
(Source: BLS 2018, www.osha.gov)

## Slide 24: Tragic Facts
60% of related deaths are rescuers
  Civilians
  Fire dept personnel
  Co-workers
Cave-ins can happen without warning
All of the fatalities and injuries could have been prevented

## Slide 25: Collapse Forces
24 inches of soil on a person’s chest weighs 750-1000 lb.
18 inches of soil covering a body weighs 1800-3000 lb.
Notes: HOW MUCH CAN YOU LIFT, how well can you breathe
HOW MANY BREATHS CAN YOU TAKE
LOCK OUT/ TAG OUT
8” WATER MAIN CAN FLOW 19,000 GPM AT 100 PSI
CAN FILL A TRENCH 4X12X25 IN 24 SECONDS

## Slide 26: Soil Weight Example
© ACR Publications Used By Permission
20 cubic feet = 2,000 lbs.
How tall are you? This example is 4ft deep
Do you think you can get out?

## Slide 27: Collapse Force
Shear wall collapse speed is 45 mph
1 cubic foot of soil can weigh from 100 to 125 lb.
Notes: THINK YOU CAN OUT RUN IT
VW HITTING YOU AT 45MPH
PAST PRACTICES
JUMP INTO TRENCH
F/F ARE ACTION ORIENTED
COMPASSION KILLS
INADEQUATE SHORING
CHEAPER TO PAY DEATH BENEFITS

## Slide 28: Speed of Collapsing Dirt
Imagine this coming down on top of you….
Weight of a Volkswagen
2,785 Pounds
Weight of one cubic yard of soil
2,700 Pounds

## Slide 29: Effects On The Body
Respiratory distress
Crush syndrome
Total body impact
Notes: How many breaths can you take with this much weight on your body, explain crush syndrome

## Slide 30: Trench collapse
Notes: If dirt can do this to a ladder?

## Slide 31: The Seven Trenching Hazards
Cave–ins
Electric Line Contact
  Overhead
  Buried
Falls into Excavations
Equipment Falling into Excavations
Explosion / Fire / Electrocution
Hazardous Atmosphere
Drowning

## Slide 32: UNSAFE ATTITUDES
“I Know what I’m doing.”
“It can’t happen to me.”
“I’ve been doing it that way for years.”
“I’d sleep in that hole!”
“Don’t worry, we’ll watch the walls and tell you if you need to get out.”

## Slide 33: Most Common Causes of Cave-ins:
Poor Planning
Misjudgment of soil type.
Inadequate, or incorrect installation of protective devices.
Defective protective devices.
Failure to adjust for changing conditions

## Slide 34: Legal Aspects
OSHA [29 CFR 1926.650 - 652]
  Excavation standard applies to all open excavations made in the earth’s surfaces including trenches, all surface encumbrances that would create a hazard, and protective systems

## Slide 35: What’s In the Standard?
Scope, application and definitions
Job Site Hazard Listing
Requirements for Protective Systems
Appendixes that detail:
  Soil Classification
  Sloping and Benching
  Timber and Aluminum Hydraulic Shoring
  Protective System Selection Decision Tree

## Slide 36: General Requirements
1926.651
(a) Surface encumbrances
(b) Underground installations
(c) Access & egress
(d) Exposure to vehicle traffic
(e) Exposure to falling loads
(f) Warning systems for mobile equipment

## Slide 37: General Requirements (CONT.)
1926.651
(g) Hazardous atmospheres
(h) Protection from hazards associated with water accumulation
(i) Stability of adjacent structures
(j) Protection from loose rock or soil
(k) Inspections
(l) Fall protection

## Slide 38: Surface Encumbrances
All surfaces encumbrances that are located so as to create a hazard to employees shall be removed or supported as necessary to safeguard employees

## Slide 39: Underground Installations
Utility companies shall be contacted with in established local response times
  Advised of proposed work
  Asked to establish location of utility
  When request cannot be met, employer may proceed with caution with detection equipment of an acceptable means to locate utility
Notes: Call before you dig: In Maryland and Delaware Dial 811

## Slide 40: Underground Installations (CONT.)
While the excavation is open, underground installations shall be protected, supported or removed as necessary to safeguard employees

## Slide 41: Access & Egress
Structural ramps
  Used by employees shall be designed by a competent person
  When used for equipment shall be designed competent person qualified in structural design
  Stairway, ladder, ramp or other safe means of egress require no more than 25 ft of lateral travel for employees in excavations that are 4 feet or more in depth
  Ladders must be secured and extend a minimum of 36 inches above the landing

## Slide 42: Exposure to vehicle traffic
Employees exposed to public vehicle traffic shall be provided with and wear warning vests or other suitable garments
  Marked or made with reflectorized or highly visible material
  Requiring a designated, trained flag person along with signs, signals, and barricades when necessary

## Slide 43: Exposure to falling loads
  No employee shall be permitted underneath loads handled by digging or lifting equipment
  Stand away from vehicle being loaded or unloaded to avoid being struck
  Operators may remain in cabs when vehicles are equipped in accordance with 1926.601

## Slide 44: stuck-in
Notes: Victim was working underneath load being moved

## Slide 45: Warning systems for mobile equipment
When operator does not have clear view of edge of excavation
Warning system shall be utilized
  Barricades
  Hand or mechanical signals
  Stop logs

## Slide 46: excavation without proper barricade
Notes: Victim was ejected from tractor into the trench (lower center )

## Slide 47: Vehicle falling in excavation
Notes: How much vibration does a concrete truck put on the side of a trench when mixing his load. Enough to cause collapse?

## Slide 48: Hazardous Atmospheres
Testing and controls
  To prevent harmful levels of atmospheric contaminants
  Less than 19.5% or more than 23.5% oxygen
  Atmosphere tested before entry
  Adequate precautions shall be taken
    Ventilation
    Proper respiratory protection
    Testing done often as necessary
Notes: TEST IN MULTIPLE LEVELS – TOP/MIDDLE/BOTTOM ( SAME AS CONFINED SPACE)

## Slide 49: exposed to hazardous atmosphere
Notes: Unshored trench with backhoe and track hoe on lip with trash pump for water removal

## Slide 50: Employees exposed to hazardous atmosphere
Notes: Worker using a cut-off saw, gas can also in excavation

## Slide 51: Monitoring
Notes: Monitoring for hazardous atmospheres

## Slide 52: Ventilation Blowers
Notes: Propane system for heated ventilation

## Slide 53: Emergency Rescue Equipment
Rescue equipment
  Breathing equipment
  Safety harness and line or basket stretcher
  Must be readily available
  Must be attended
  Bell-bottom pier holes, deep and confined footing excavation shall wear a harness with a lifeline securely attached to it

## Slide 54: BELL BOTTOM PIER HOLE
A tubular shaft with a wider bell shaped cross-section at it’s base for support. Created for foundations and footer construction.

## Slide 55: Water Accumulation
Notes: How much water is to much?

## Slide 56: Water Accumulation (CONT.)
Employees shall not work in excavations where there is accumulated water, or where water is accumulating, unless adequate precautions have been taken, to protect employees.
Must take adequate precautions to protect employees
  Accumulating water
  Varies with each situation
  Removal monitored by competent person
  Run off from heavy rains requires inspection by competent person

## Slide 57: Water removal from trench
Notes: Well point system to lower ground water, pipes placed in ground to pump out water

## Slide 58: Water removal equipment
Notes: Trash pump, watch were discharged water goes

## Slide 59: Stability of adjacent structures
Where stability is endangered by excavation operations
Support systems such as shoring, bracing or underpinning shall be provided
Sidewalks, pavement and appurtenant structures shall not be undermined unless support systems are used to protect employees

## Slide 60: No support provided to prevent structural failure
Notes: Is the backhoe supporting the house or the house supporting the backhoe

## Slide 61: Support provided under the ground level
Notes: Worker buried up to his waist, beneath concrete and brick veneer collapsing

## Slide 62: Protection from loose rock and soil
Hazard from falling or rolling from excavation face
  Scaling to remove loose materials
  Installation of protective barricades
  Other means (retaining devices)
  2 feet from edge of excavation

## Slide 63: Trench
Notes: How many things are wrong here?

## Slide 64: What’s good?
WHAT’S NOT SO GOOD?
Notes: Good – protective system in place, ladder, water removal, no one under moving load.

## Slide 65: WHO IS Competent Person
One who is capable of identifying existing or predictable hazards in the surroundings which are unsanitary, hazardous or dangerous to employees & who has authorization to take prompt corrective measures

## Slide 66: Competent Person
Has specific training in and be knowledgeable about soil analysis, use of protective systems and the requirements of the standard

## Slide 67: COMPETENT PERSON MUST BE AWARE OF:
Falling loads or equipment
Hazardous atmospheres
Weather conditions and forecast
Stability of adjacent structures.

## Slide 68: THE COMPETENT PERSON MUST BE AWARE OF:
Surface and overhead encumbrances
Underground utilities
Access and egress
Vehicular traffic
Continuation of trade activity

## Slide 69: Inspections
Daily and before start of work
As needed throughout the shift
After snowstorms, windstorms, thaw, earthquake
Soil classification
Any hazard increasing occurrence
Employees shall be removed until precautions have been taken

## Slide 70: Inspections (CONT.)
When fissures, tension cracks, sloughing undercutting, water seepage, bulging at the bottom
Change in size, location or placement of the spoil pile
Indication of movement in adjacent structures

## Slide 71: Hazard
Notes: Who inspected this trench? Ladder to short, no protective system, soil pile to close

## Slide 72: Training, knowledge and experience as demonstrated through responsible action makes a person “competent.”

## Slide 73: Fall protection
If walkway provided
  Where employees permitted to cross, guard rails provided where 6 feet or more above lower levels
  Fall protection standard
Notes: This refers to guard rails (1926.502(b)

## Slide 74: Requirements of Protective Systems
1926.652
Employees shall be protected from cave-in by an adequate protective system except;
  Entirely in stable rock
  Less than 5 feet in depth with no indication of cave-in

## Slide 75: No proper protection
Notes: The proper use of a protective system? 10 ft trench box in a 26ft deep hole, a fatality happened here.

## Slide 76: PROPER SHORING
Notes: How many laws are broken here? Screw Jack used for cross member must be in trench to install

## Slide 77: Designs using Manufacturers Data
Deviation will only be allowed after manufacturer issues specific written approval
Written form at the job site during construction

## Slide 78: Materials and Equipment
Free of damage and defects
Maintain in manner consistent with manufactures data
Examined by competent person & evaluated for continued use
Removed from service until approved by registered professional engineer

## Slide 79: Trench box
Notes: How much abuse can you do to a shield before it fails?

## Slide 80: Trench Boxes
Notes: Make sure all cross members and safety pins are used when necessary

## Slide 81: Installation & Removal
Members securely connected
  Prevent sliding, falling, kick outs
  Other predictable failure
Members shall not subjected to loads exceeding those which were designed
Members removed from bottom first
Back fill with removal of support system

## Slide 82: Installation & Removal (CONT.)
Excavate to no greater than 2 feet below – only if system is rated at full depth and there are no indications of a loss of soil from behind or below the support system
Employees are not permitted to work below other employees unless adequately protected from falling, rolling, sliding material
Employees are not allowed in shields when installed, removed or moved vertically

## Slide 83: Removal of trench box
Notes: When an inspector is doing this something bad has happen.

## Slide 84: PICTURE OF Trench
Notes: Not a certified trench box. Made by laborers on site

## Slide 85: PROPER Trench box
Notes: Safe or not?

## Slide 86: Shield testing
Notes: Nice system for shallow trenches 130 lbs overall weight

## Slide 87: Shield testing by competent person

## Slide 88: GUESS
WHAT’S NOT SO GOOD?
WHAT’S GOOD?
Notes: Unsupported utilities, no ladder, how much vibration does a freight train make?

## Slide 89: Shield Used with Sloping
Notes: Unsupported utilities, no ladder, how much vibration does a freight train make?

## Slide 90: Horizontal Shoring Dimensions
© ACR Publications Used By Permission

## Slide 91: Vertical Shoring Dimensions
© ACR Publications Used By Permission

## Slide 92: Pneumatic Systems
Notes: Pneumatic system to mechanical

## Slide 93: SHIELD USAGE AND SAFETY Shields are used to protect workers from cave-ins, not to provide support for the trench.
Manufacturer’s Data must be present at work site.
Top of the shield must extend to the top of the trench.
If used with sloping, top of shield must extend 18 inches above vertical trench walls.
Shields may be stacked, provided the bottom one is rated for the total depth of the trench.
The trench may be dug 2 feet lower than the shield bottom, but the shield must be rated for that depth.
Backfill around the box to prevent lateral movement.
Notes: Trench boxes must be designed to be stacked.You can put any box on top of another

## Slide 94: Soil Classification 1926 Subpart P App A
Cemented soil
Cohesive soil
Dry soil
Fissured
Granular soil
Layered system
Moist soil
Plastic
Saturated soil
Soil classification system
Stable rock
Submerged soil
Unconfined compressive strength
Wet soil

## Slide 95: Soil Category: Stable Rock
Natural solid mineral material that can be excavated with vertical sides and remain intact while exposed. Examples are granite and sandstone.
Determining whether a deposit is stable rock may be difficult unless it is known whether cracks exist and whether or not the cracks run into or away from the excavation.

## Slide 96: Soil Classifications
Stable rock
Type A
Cohesive soils with an unconfined compressive strength of 1.5 tons per square foot [tsf]
Examples: Clay, silty clay, sandy clay
Notes: NO SOIL IS A, IF FISSURED, SUBJECT TO VIBRATION,
PREVIOUSED DISTURBED,SEEPING WATER
SOIL TEST VISUAL-
SIDES OF TRENCH FOR LAYERING
EVIDENCE OF WATER
PREVIOUSLY DIETURBED SOIL
TENSION CRACKS, SPALLING, BOILING
MANUAL TEST
PLASTICITY
DRY SRRENGTH
THUMB PRENETRATION

## Slide 97: Soil Classifications (CONT.)
No soil is type A if;
  Fissured
  Subject to vibration
  Previously disturbed
  Seeping water
  Part of a sloped or layered system of four horizontal to one vertical

## Slide 98: Soil Fissuring
Notes: How soon will it fail?

## Slide 99: To Much Water?
Notes: What do you have to do to make this trench safe?

## Slide 100: Weight and Vibration
Notes: How much pressure does it take from an outrigger to make this trench fail

## Slide 101: Soil TYPES
Type B
  Cohesive soils with an unconfined compressive strength greater than 0.5 tsf but less than 1.5 tsf
  Silt, silt loam, angular gravel
  Soils that are fissured, or subject to vibration
Notes: PREVIOUSLY DISTURBED UNLESS CLASSIFIED AS C. Define Silt and Loam type soils

## Slide 102: Soil Classification
Type C
Cohesive soils with a unconfined compressive strength of 0.5 tsf or less.
  Gravel, sand, loamy sand, submerged soil, soil from which water is freely seeping

## Slide 103: SOIL STRENGTH MEASURE Unconfined Compressive Strength (UCS)
The amount of pressure in tons per square foot (tsf) required to cause the soil to fail in compression.
OSHA Soil Classification is based on the UCS of the soil.
Notes: Tests are usually done in the lab.

## Slide 104: Basis of classification
The classification of deposits shall be made based on the results of at least one visual and one manual analysis conducted by a competent person

## Slide 105: Acceptable visual test
Determine qualitative information on site in general
Soil adjacent to excavation
Soil forming the sides of the open excavation
Soil taken as samples from excavated material
Estimate range of particle sizes

## Slide 106: Acceptable visual test CONT.
Observe evidence of surface water
Water seeping from the sides
Location of the level of the water table
Sources of vibration that may affect stability
Evidence of previously disturbed soil

## Slide 107: Acceptable manual test
Plasticity
Ribbon and thread test
Dry strength test
Thumb penetration test
Other strength test
Pocket pentrometer
Hand-operated shearvane

## Slide 108: Field Sedimentation Test
Flat bottom container - at least 7 inches high (old olive jar)
One 1/2 to 2 inches of soil
Place soil in the glass jar
5 inches of water on top of soil

## Slide 109: Field Sedimentation Test (CONT.)
After 30 seconds granular sand type material settles at the bottom
After 3 minutes silt type material settles on top of the sand

## Slide 110: CLAY, SAND AND SLIT

## Slide 111: The Ribbon Test step 1
Mix soil + water to make into plastic mass
Roll mass into cylindrical shape 1/2 to 3/4 inch diameter
Lay across palm of hand
Press between thumb and second joint of index finger

## Slide 112: The Ribbon Tests STEP 2
Pass through thumb
Squeeze until it takes the shape of a 1/8 to 1/4 inch thick strip
Allow to hang freely from hand

## Slide 113: The Ribbon Test (cont.)
Clay loam will barely ribbon and break easily
Clay = relatively long ribbon 6” to 8” or more
More clay = longer and stronger ribbon
Silt has tendency to produce short ribbon with broken appearance

## Slide 114: PENCILING
If a 2 inch or longer thread can be held without breaking, the soil is cohesive.

## Slide 115: Shear vane / Torvane
Measures Soil’s Shear Strength

## Slide 116: Shear vane / Torvane
Select fresh clod or block of undisturbed soil from spoil pile
Cut a smooth surface on the clod
Insert vanes of device into the soil
Retract vanes to show foot imprint
Set indicator at zero
Hold device firmly against soil and twist in clockwise manner until soil fails in shear

## Slide 117: Pocket Penetrometer Test
Device is designed to work on saturated clay soil
Measures unconfined compressive strength of soil
Twice the value of shear strength of same soil
Note machine ring

## Slide 118: POCKET PENETROMETER

## Slide 119: Pocket Penetrometer Test
To begin test, remove red protective cap, push ring against body so that low side reads “O”
Slowly insert piston until engraved mark is level with soil

## Slide 120: Pocket Penetrometer Test (CONT.)
Read strength in tons/sq ft using low side of ring (side closest to the piston end). Record reading and repeat step #1.
For weak soils, use 1” adaptor foot, multiply by 0.0625

## Slide 121: Thumb Penetration Test
The thumb penetration procedure involves an attempt to press the thumb firmly into the soil in question.
Notes: OSHA TECHNICAL MANUAL – SECTIONV: CHAPTER2

## Slide 122: Thumb Penetration Test (CONT.)
If the thumb makes an indentation in the soil only with great difficulty, the soil is probably Type A.
If the thumb penetrates no further then the length of the thumb nail, it is probably Type B soil.
If the thumb penetrates the full length of the thumb it is Type C soil.
The thumb test is subjective and is therefore the least accurate of the tests.
Notes: OSHA TECHNICAL MANUAL – SETION V: CHAPTER 2

## Slide 123: Soil Classifications.
Layered Geological Strata
  where soils are configured in layers
  must be classified on the basis of the weakest soil
  each layer may be classified individually if a more stable layer lies below a less stable layer
  Type C soil rests on top of stable rock

## Slide 124: CLASSIFICATION
Look for the following conditions
  Particle size
    Primarily fine grained=cohesive material
    Primarily coarse-grained sand or gravel
    Granular material
  Cohesion
    Remains in clumps=cohesive

## Slide 125: Soil Strength is Dependent Upon:
Type of Soil.
Amount of Moisture in the Soil.
Whether the Soil Has Been Previously Disturbed.

## Slide 126: If Water is Added
It Brings Additional Weight
  Hydrostatic Pressure
It Erodes the Trench Wall
  Water movement typically moves soil
It Can Freeze and Thaw
  Resulting in cracks & false cohesion
REMOVAL OF GROUND WATER IS CRITICAL

## Slide 127: SOIL COMPONENTS
Clay:
  Composed of mineral particles less than 0.002 mm in diameter
Silt:
  Individual mineral fragments that range from 0.002 to 0.05 mm in diameter.
Sand:
  Individual rock or mineral fragments that range in diameter from 0.05 to 2.0 mm in diameter.
Gravel:
  Can be either angular or rounded.

## Slide 128: COHESIVE SOIL
Soil with a high clay content which has cohesive strength.
It does not crumble.
It can be excavated with vertical side slopes.
It is hard to break up when dry.
It can be molded.
It exhibits significant cohesion even when submerged.

## Slide 129: GRANULAR SOIL
Soils that include gravel, sand, silt.
Very low clay content.
It has no cohesive strength.
Some moist granular soils exhibit apparent cohesion.
It cannot be molded when moist and crumbles easily when dry.

## Slide 130: Soil Mechanics
Toppling occurs when the trench’s vertical face shears along the tension crack line and topples into the excavation

## Slide 131: TOPPLING
Notes: Toppling into the trench

## Slide 132: SUBSIDENCE
Subsidence and bulging occurs when an unsupported excavation can create an unbalanced stress in the soil which causes subsidence at the surface and bulging of the vertical face

## Slide 133: UNSUPPORTED EXCAVATION
Notes: Can the weight of this crane cause bulge or failure

## Slide 134: bulging
Notes: Where is the crane. Is the gas line supported. What shoring?

## Slide 135: Soil Mechanic
Heaving or squeezing is caused by the downward pressure created by the weight of adjoining soil or equipment
Can occur even when shoring or shielding has been properly installed

## Slide 136: Forces Acting on a Trench
© ACR Publications Used By Permission

## Slide 137: BOILING
Boiling is evidenced by an upward water flow into the bottom of the cut
High water table is one cause
Boiling produces a quick condition even when trench boxes are used

## Slide 138: Trench Boiling
Notes: Boiling and toe failure

## Slide 139: TRENCH CRACK
Tension cracks usually form at a horizontal distance of 0.5 to .75 times the depth of the trench
Tension Crack

## Slide 140: SLIDING
Sliding or sloughing may occur as a result of tension cracks
Sliding

## Slide 141: Sloping and Benching 1926 Subpart P App B
Actual slope
Distress
Maximum allowable slope
Short term exposure
Stable rock
Type A soil
Type B soil
Type C soil

## Slide 142: Design of Sloping and Benching
Allowable configurations and slopes
  Not steeper than 11/2 horizontal to 1 vertical
  Designs using other tabulated data
  Shall be in written form
  Must identify limits of use of the data
  Identify the registered professional engineer who approved

## Slide 143: IMPROPER Design
Notes: An attempt at sloping?

## Slide 144: IMPROPER Sloping
Notes: Benching?

## Slide 145: Allowable Slopes
Type A Short term
½ to 1 height/depth and 63 degree slope
Max excavation depth 12 ft
Soil Type | Height/ Depth | Slope angle
Stable Rock | Vertical | 90 Degree
Type A | ¾ to 1 | 53 Degree
Type B | 1 to 1 | 45 Degree
Type C | to 1 | 34 Degree
Soil Type | Height/ Depth | Slope angle
Stable Rock | Vertical | 90 Degree
Type A | ¾ to 1 | 53 Degree
Type B | 1 to 1 | 45 Degree
Type C |  | 34 Degree

## Slide 146: Examples of Sloping for Different Soils

## Slide 147: BENCHING
Only to be used on soil types A and B
Type A
Type B

## Slide 148: SOIL TYPE A
Type A soil
Supported of shielded vertically sided lower portion
¾ to 1
20 feet max depth
Shield 18 inches above to prevent rollover

## Slide 149: SOIL TYPE B
Type B soil
Supported of shielded vertically sided lower portion
1 to 1 sloped
18 inches minimum at top of shield to prevent rollover
Type B
Soil Supported of shielded vertically sided lower portion

## Slide 150: SOIL TYPE C
Type C soil supported of shielded vertically sided lower portion
1 ½ to 1
20 feet max depth
18 inches above to prevent rollover

## Slide 151: Slope Configurations Excavations in Layered Soils

## Slide 152: Slope Configurations Excavations in Layered Soils

## Slide 153: Excavations in Type A Soils

## Slide 154: Timber Shoring for Trenches 1926 Subpart P App C
Basis and limitations of data
  Trenches do not exceed 20 ft in depth
  Each table presents the minimum sizes of timber members to use in a shoring system
  Tables are taken from National Bureau of Standards

## Slide 155: EG 1: Timber shoring
Notes: Timber system being built

## Slide 156: EG 2 : Timber Shoring
Notes: Timber system in place

## Slide 157: Timber Shoring

## Slide 158: Aluminum Hydraulic Shoring 1926 Subpart P App D
Basis and limitations of data
  Vertical shore rails and horizontal wales
  Meet equivalent strength properties
  2 inch cylinder inside diameter minimum safe working capacity of no less than 18000 lbs compressive load at maximum extension
  3 inch cylinder inside diameter safe working load not less than 30000 lbs axial compressive load
  Vertical shores used must be minimum of 3 spaced equally

## Slide 159: Aluminum Hydraulic
Vertical Aluminum Hydraulic Shoring
(Spot Bracing)
Aluminum Hydraulic Shoring Water System
(With Plywood)

## Slide 160: STACKED AND TYPICAL Hydraulic
Vertical Aluminum Hydraulic Shoring
(Stacked)
Aluminum Hydraulic Shoring Water System
(Typical)

## Slide 161: EG 1: Aluminum Hydraulic
Notes: Aluminum hydraulic shoring

## Slide 162: EG 2: Aluminum Hydraulic
Notes: Aluminum hydraulic shoring

## Slide 163: Spot-bracing Usage
Notes: Aluminum hydraulic shoring

## Slide 164: Hydraulic Shoring Usage

## Slide 165: Alternatives to Timber Shoring 1926 Subpart P App E
Pneumatic & Hydraulic Jacks
Screw Jack

## Slide 166: Alternatives to Timber Shoring (CONT.)

## Slide 167: HYDRAULIC CYLINDER

## Slide 168: aluminum hydraulic shoring
Notes: Pneumatic shoring with ventilation being used in rescue

## Slide 169: Other Factors Influencing Cave-Ins
Intersecting Trenches
Previously Disturbed
Vibration
Surcharged Load
Inclined Layers
Drying / Saturation
Free standing time

## Slide 170: 1. Fallacies And Misconceptions
At what depth/width do most incidents occur?
  Most utilities found in this area: Between 6-8 ft deep and less than 6 ft wide

## Slide 171: 2. Fallacies And Misconceptions
Most incidents occur in bad weather
  False
  Good weather
  Crews are more careful in bad weather
Notes: FREEZING GROUND THAWING
DRYING OUT
WARM TURNING COLD

## Slide 172: 3. Fallacies And Misconceptions
Clay is the least dangerous soil type
  False
  Clay looks strong but it is very deceptive most fatal trench accidents occur in clay soil

## Slide 173: THE TYPICAL CAVE-IN
© ACR Publications Used By Permission

## Slide 174: Summary
Excavation laws, regulations, standards
Soil classification
Soil testing
Competent person responsibilities
Hazards associated with trenches
Protective systems