## Slide 1: Fall Hazards
This material was produced under Susan Harwood Grant Number SH-31220-SH7 from the Occupational Safety and Health Administration, U.S. Department of Labor. It does not necessarily reflect the views or policies of the U.S. Department of Labor, nor does mention of trade names, commercial products, or organizations imply endorsements by the U.S. Government.
Fall Prevention in Construction
Susan Harwood Grant FY 17
SH-31220-SH7

## Slide 2: Introduction
The following presentations have been developed in both Spanish and English for the construction industry. These presentations focus in fall Hazards in construction.
This training materials will cover the fall hazards seen regularly on construction sites and will focus on the methods for the recognition and the prevention of these common hazards.

## Slide 3: Fall Hazards - Overview
Fall Hazards
Building Structures
Exterior Construction Areas
Accident Prevention
Guardrails
Scaffolds
Stairs
Ladders
Warning Lines
Personal Fall Arrest Systems
Floor Covers

## Slide 4: Fall Hazards
The symbols will tell you if the situation in the picture is either safe or not safe.
Falls are one of the greatest hazards on construction sites.
This program will help you recognize common fall hazards.

## Slide 5: Fall Hazards Statistics
Each year workers die from falls. During the year 2015:
  Total deaths from falls: 648
  Deaths in construction: 298
  A total of 46% of deaths in Construction are from falls
  Approximately 13% of all occupational deaths are falls

## Slide 6: Fall Hazards
Fall hazards can be found on every construction site:
Building structures
Exterior construction areas
Scaffolds
Stairs
Ladders

## Slide 7: Building Structures
Work conditions 6’ or more above lower level require the use of fall protection:
Unprotected sides, edges
Leading edges
Excavations
Walking/working surfaces

## Slide 8: Building Structures
This worker is working 6’ above the lower level without using fall protection.

## Slide 9: Building Structures
  Personal fall arrest systems
  Guardrails
When working at a height of 6’ above the lower level you must use fall protection:

## Slide 10: Building Structures
When working at a height of 6’ above the lower level you must use fall protection.
These workers are not utilizing a personal fall arrest system.

## Slide 11: Building Structures
Guardrails must be maintained when working 6’ above lower level.

## Slide 12: Building Structures
Damaged or missing guardrails must be fixed immediately.

## Slide 13: Exterior Construction Areas
Falls from a short distance can result in serious injury.
All workers must be protected from falling onto sharp materials.

## Slide 14: Exterior Construction Areas
All open excavations and pier holes must be guarded or protected.

## Slide 15: Scaffolds
  Supported scaffold
  Guardrails
  Access ladders
  Powered work platforms
Scaffolds are elevated,temporary work platforms:

## Slide 16: Scaffolds
Scaffold bases must rest on a base plate and a mud sill.
The base plate is designed to level and support the scaffold.

## Slide 17: Scaffolds
Only work from scaffolds that are properly constructed and supported.

## Slide 18: Scaffolds
Scaffolds used in stair wells must be properly constructed.

## Slide 19: Scaffolds
When working on scaffolds 6’ above lower level, guardrails must be installed.

## Slide 20: Scaffolds
Never use scaffolds that do not have proper guardrails installed.

## Slide 21: Scaffolds
Scaffold platforms must be fully and properly planked

## Slide 22: Scaffolds
Never stack blocks, bricks, or use ladders on top of scaffolds for extra height.

## Slide 23: Scaffolds
Workers must have a safe way to access the scaffold.

## Slide 24: Scaffolds
Never use blocks, bricks, walk boards, and other unsafe methods to access a scaffold.

## Slide 25: Scaffolds
Use only ladders designed for use with scaffolds.
The ladder must be firmly secured to the scaffold.

## Slide 26: Powered Work Platforms
man-baskets placed on a forklift,
aerial lifts, and
scissor lifts.
Powered platforms include:

## Slide 27: Powered Work Platforms
Always make sure you have proper fall protection and training before using a powered platform.

## Slide 28: Powered Work Platforms
  Only use equipment that is designed for lifting personnel.

## Slide 29: Stairs
Stairways must have a stair rail along each unprotected side or edge.

## Slide 30: Stairs
Stairs that have walls on both sides must have at least one hand rail on the right-hand side when climbing down.

## Slide 31: Ladders
Never use stairs that are not complete or unsafe.

## Slide 32: Ladders
Ladders must be inspected prior to use.
Ladders must be
kept in a good
condition and safe
location.

## Slide 33: Ladders
Do not stand on the top of a ladder.

## Slide 34: Ladders
Read labels on ladders for instructions to ensure proper use

## Slide 35: Ladders
Always maintain good footing on a step ladder.
Use the correct size ladder for the work that is to be done.

## Slide 36: Ladders
Ladders
Lifts
Scaffolds
Always use the right equipment for the job:

## Slide 37: Ladders
Never straddle or sit on top of a step ladder.

## Slide 38: Ladders
An A-Frame ladder must be fully opened and locked into position.
Use ladders only for their designed purpose.

## Slide 39: Ladders
Only use ladders on stable and level surfaces to prevent accidental movement.

## Slide 40: Ladders
Ladders must be positioned at a safe angle to avoid potential fall hazards when climbing.
Extension ladders must extend 3’ over the landing for safe access.

## Slide 41: Ladders
When using a portable ladder for access to an upper landing surface, the side rails must extend at least 3’ above the upper landing surface.

## Slide 42: Ladders
  Proper use
vs.
  Improper application

## Slide 43: Ladders
Maintain contact with the ladder using both hands to keep a safe grip.
Face ladder when going up or down.
Never climb a ladder while carrying any materials.

## Slide 44: Job Made Ladders
Steps equally spaced
No missing steps or rungs
No sharp edges or nails sticking out
Job made ladders must be properly constructed:

## Slide 45: Job Made Ladders
Never use a job made ladder that is damaged or missing steps.
Only use a job made ladder that has been properly built.

## Slide 46: Job Made Ladders
Job made ladders must also be constructed so that no nails protrude or sharp edges exist.
Nails and sharp
edges can catch on
clothing and cause
falls.

## Slide 47: QUIZ
You will be presented with a specific hazard recognition question to test your understanding of this material.

## Slide 48: Question 1
Before using a ladder, inspect it for which of
the following?
Cracks in the frame
Broken or missing rungs
Oil, grease or other substances on the rungs
All of the above

## Slide 49: Question 1
Before using a ladder, inspect it for which of
the following?
The correct answer is:
D – All of the above

## Slide 50: Question 2
Job made ladders may be used if the steps are equally spaced with no steps missing and no sharp edges or nails sticking out.
  True
  False

## Slide 51: Question 2
Job made ladders may be used if the steps are equally spaced with no steps missing and no sharp edges or nails sticking out.
The correct answer is:
A - True

## Slide 52: Question 3
When erecting scaffolding, the base plate must be placed on what?
  A Firm Foundation
  Cement Blocks
  Soft Dirt
  Wood Blocks

## Slide 53: Question 3
When erecting scaffolding, the base plate
must be placed on what?
The correct answer is:
A – A Firm Foundation

## Slide 54: Question 4
When working on scaffolding and you need a little more height, you must do the following:
  Stand on a saw-horse
  Jump
  Erect another section of scaffolding
  Use a ladder

## Slide 55: Question 4
When working on scaffolding and you need a little more height, you must do the following:
The correct answer is:
C – Erect another section of scaffolding

## Slide 56: Question 5
Stairs that are incomplete and missing handrails are acceptable to use during the construction phase of the project.
  True
  False

## Slide 57: Question 5
Stairs that are incomplete and missing handrails are acceptable to use during the construction phase of the project.
The correct answer is:
B – False

## Slide 58: Accident Prevention
A willing, positive attitude towards safety will help make a safer work environment.

## Slide 59: Preventing Fall Accidents
Construction work performed at 6’ or higher above a lower level requires fall protection.
Some fall protection methods include:
  Guardrails
  Warning lines
  Fall arrest systems and
  Floor covers

## Slide 60: Guardrails
Guardrails must have a top rail, a mid rail and a toe board.
The top rail must be at least 42” from the working surface.

## Slide 61: Guardrails
All guardrails must be constructed with a top rail and a mid rail.
The top rail must support 200 lbs. of force downward and outward.

## Slide 62: Guardrails
Cable guardrails must meet the same rules as wood guardrails.
The top rail must be at least 42” high and resist up to 200 lbs.

## Slide 63: Cable Guardrails
Steel cable guardrails must have the top rail flagged every 6 feet.

## Slide 64: Cable Guardrails
The clamps used for a steel cable system must be placed correctly.

## Slide 65: Warning Lines
Warning lines are used to keep workers away from an unsafe edge.
The warning line must be at least 6’ away from the edge.

## Slide 66: Warning Lines
Warning lines must withstand 16 lbs. of tipping force.
The warning line must be at least 34” from the ground.

## Slide 67: Warning Lines
Warning lines must be maintained.
Report any unsafe condition to your supervisor.

## Slide 68: Warning Lines
Never work in an area if the warning line has been knocked down or damaged.

## Slide 69: Personal Fall Arrest Systems
  body harness,
  lanyard, and
  anchorage point
The fall arrest system components are:

## Slide 70: Personal Fall Arrest Systems
Body harness must be worn properly.
D-ring must rest between the shoulders and the chest strap must be secured.

## Slide 71: Personal Fall Arrest Systems
  inspected before use,
  adjusted to fit the worker, and
  free from other visible damage.
Body harness must be:

## Slide 72: Personal Fall Arrest Systems
Lanyards must be in good condition and free from visible damage.

## Slide 73: Personal Fall Arrest Systems
Lanyard must attach to the D-ring on the body harness.

## Slide 74: Personal Fall Arrest Systems
Never anchor or tie
off to pipes, wood structures, electrical wires, or other areas not designed for anchorage points.

## Slide 75: Personal Fall Arrest Systems
The anchorage point is the place where you tie off to or hook to.
The anchorage point must support the force of a person falling.

## Slide 76: Personal Fall Arrest Systems
A life line is used to allow a worker to stay tied off while he moves through the work area.

## Slide 77: Personal Fall Arrest Systems
Workers must always be tied off when working with a personal fall arrest system.

## Slide 78: Floor Covers
The cover must be marked to make sure everyone knows it is a safety device.

## Slide 79: Floor Covers
All floor holes where an employee could fall through must be covered or guarded.

## Slide 80: Floor Covers
Sky-lights are another form of floor holes.
Never sit, stand, or place any materials on sky-lights.

## Slide 81: Floor Covers
Pier holes must be guarded or protected.
Either a guard rail system or floor hole cover can be used.

## Slide 82: QUIZ
You will be presented with a specific accident prevention question to test your understanding of this material.

## Slide 83: Question 1
While working in the construction industry, at what height is fall protection required?
  4 feet
  10 feet
  6 feet
  8 feet

## Slide 84: Question 1
While working in the construction industry, at what height is fall protection required?
The correct answer is:
C – 6 feet

## Slide 85: Question 2
Guardrails are designed to protect you from falling. The top rail must be inches high and be able to withstand pounds of force.
  42 / 300
  36 / 300
  42 / 200
  36 / 200

## Slide 86: Question 2
Guardrails are designed to protect you from falling. The top rail must be inches high and be able to withstand pounds of force.
The correct answer is:
C – 42 / 200

## Slide 87: Question 3
Guardrails can be made of wood or steel cables. When using steel cables the cable clamps must be placed:
  In alternating directions
  With the U-bolt on the dead end of the cable
  With the saddle on the dead end of the cable
  None of the above, clamps are not required

## Slide 88: Question 3
Guardrails can be made of wood or steal cables. When using steal cables the cable clamps must be placed:
The correct answer is:
B – With the U-bolt on the dead end of the cable

## Slide 89: Question 4
When inspecting a harness before using it, you
should look for the following:
  Cuts/Abrasions
  Burns
  Other visible damage
  All the above

## Slide 90: Question 4
When inspecting a harness before using it, you should look for the following:
The correct answer is:
D – All the above

## Slide 91: Question 5
Floor holes can include which of the following:
  Pier holes, skylights and stair openings
  Pier holes, skylights and window openings
  Skylights, stair openings and doorways
  Skylights, stair openings and open sided floors

## Slide 92: Question 5
Floor holes can include which of the following:
The correct answer is:
A – Pier holes, skylights and stair openings

## Slide 93: Thank You For Attending!
Questions