## Slide 1: Global harmonization system & overview of Chemical hazards in the oil & Gas industry
This material was produced under grant number SH-31238-SH7 from the Occupational Safety and Health Administration, US Department of labor. It does not necessarily reflect the views or policies of the US Department labor, nor does mention of trade names, commercial products, or organizations imply endorsement by the US Government.

## Slide 2: Training pre-assessment
How much do you already know about chemical hazards?
True or False:
  Hazard communication programs tell you about chemical hazards in your workplace.
  Hazard communication only tells you about health hazards for a chemical.
  GHS is a system for classifying & labeling chemicals.
What are the ways a chemical can enter your body?

## Slide 3: Overview of Chemical Hazards

## Slide 4: Chemical Hazard communication
Hazcom is a company-specific program
Tells employees about:
  Workplace chemical hazards in their work areas
  Effects of chemicals
  How to protect yourself
Source: Globally Harmonized system of Classification and Labelling of Chemicals. Available at: https://en.wikipedia.org/wiki/GHS_hazard_pictograms

## Slide 5: Health Hazards
Any chemical that can do harm to your body
Most industrial/commercial chemicals can harm you, depends on
  How much gets into your body (dose)
  How the chemical enters the body (pathway)
  Physical form of the chemical (state of matter)
  How toxic the chemical is (poisonous)
Toxicity
Dose

## Slide 6: How chemicals can enter the body

## Slide 7: Chemical Toxicity
Dose
  The seriousness of the effect depends on how much gets into the body
Acute toxicity
  The chemical causes effects quickly with/after exposure
Chronic toxicity
  The chemical causes effects after repeated or long-term exposure
Target
  The chemical can cause effects in the whole body or to a specific organ or system
  Kidney, liver, brain, heart, lungs, & circulatory system

## Slide 8: Types of toxicity
Carcinogen
  Chemicals that are known or suspected to cause cancer
Mutagenicity
  Chemicals that cause changes in genes
  Can lead to cancer or genetic changes could be passed onto children
Reproductive toxicity
  Chemicals can affect fertility and/or harm developing babies and can lead to birth defects or death
Sensitizers
  With repeated exposure smaller amounts can cause a reaction and the reaction can become more serious, possibly producing allergic type reaction
Target organ toxicity
  Chemical causes damage to a specific organ or system in the body

## Slide 9: Question / Response 1
Which of the following does not effect how hazardous a chemical is:
  How much gets into your body (dose)
  How the chemical enters your body (pathway)
  Color of the chemical (appearance)
  How toxic the chemical is (poisonous)
Chart: 
| How much gets into your body (dose) | How the chemical enters your body | Color of the chemical | How toxic (poisonous) the chemical is
001 | 0.5 | 0.5 | 0 | 0
Question / Response 1
10

## Slide 10: Answer 1

## Slide 11: physical Hazards – corrosives
Can cause burns and/or irritation
  Skin
  Eyes
  Lungs & respiratory tract if inhaled
Seriousness of burn depends on
  Time exposed
  Concentration of chemical
Can breakdown storage container if stored
incorrectly

## Slide 12: physical Hazards – Flammables & Explosives
Chemicals that can burn or explode
Concentration must be in explosive range
  Above the Lower Explosive Limit (LEL — too lean to burn)
  Below the Upper Explosive Limit (UEL — too rich to burn)
    Be aware that in rich atmospheres, incomplete ventilation may result in lowering the flammable concentration to the explosive range
100%
0%
Non-Explosive (too rich)
LEL
UEL
Explosive Range (5-17%)
Non-Explosive (too lean)

## Slide 13: physical Hazards – oxidizers
Chemicals that increase flammability or explosiveness of other chemicals
Produce or release oxygen
May or may not be flammable/explosive themselves, but greatly accelerate the flammability or explosiveness of another substance
Oxygen
Dispersion
Fuel
Confinement
Ignition

## Slide 14: Physical Form of chemical
Effects on health & physical hazards
  How chemical enters body
  How chemical reacts with itself & its surroundings
Solid
  Can be broken down into dusts
  Can form fumes or fibers when heated or abraded
Liquid
  Can be broken down into vapors, fogs, and mists
Gas
  In gaseous state naturally or upon application of heat
    and/or pressure

## Slide 15: Question / Response 2
Based on the chart shown for natural gas (methane), will it explode if the concentration in air is 50%?
Yes
No
Chart: 
| Yes | No
002 | 1 | 0
Question / Response 2
100%
0%
Non-Explosive (too rich)
LEL
UEL
Explosive Range (5-17%)
Non-Explosive (too lean)
10

## Slide 16: Answer 2

## Slide 17: Global Harmonization System

## Slide 18: What is GHS
Globally Harmonized System of Classification & Labeling of Chemicals
Communicates
  Health hazards
  Physical hazards
  Environmental hazards
Requirements for
  Product label
  Product Safety Data Sheet (SDS)
  Worker training

## Slide 19: Product Label: Required elements
Name or product identifier
Signal word
  Danger or Warning
Hazard statement
Pictogram(s)
Precautionary statement
Contact information of manufacturer
  Name, address, telephone

## Slide 20: Sample Label

## Slide 21: pictograms

## Slide 22: Pictograms (Cont.)
PHYSICAL HAZARDS

## Slide 23: Pictograms (Cont.)

## Slide 24: Pictograms (Cont.)

## Slide 25: Pictograms (Cont.)

## Slide 26: Pictograms (Cont.)

## Slide 27: Pictograms (Cont.)

## Slide 28: Pictograms (Cont.)
HEALTH HAZARDS

## Slide 29: Pictograms (Cont.)

## Slide 30: Pictograms (Cont.)

## Slide 31: Pictograms (Cont.)

## Slide 32: Pictograms (Cont.)

## Slide 33: 14
Which of the following pictograms means health hazard?
A
B
C
D
Chart: 
| A | B | C | D
003 | 0 | 1 | 0 | 0
Question / Response 3
10

## Slide 34: Answer 3

## Slide 35: signal word
Only one signal word on label
  Picked based upon the most serious hazard
Danger
  More serious hazards
Warning
  Less serious hazards

## Slide 36: statements
Hazard Statement(s)
  Type of hazard from chemical
  Level of hazard
Precautionary Statement(s)
  Prevention
    Ways to minimize exposure
    Ways to minimize hazards
  Response
    Spills, first-aid
  Storage
  Disposal

## Slide 37: Product Safety Data Sheets (SDS) Required & optional sections
Identification
Hazard identification
Information on ingredients
First-aid measures
Fire-fighting measures
Accidental release measures
Handling & storage
Exposure controls/Personal protection
Physical & chemical properties
Stability & reactivity
Toxicological information
Ecological information (Optional)
Disposal considerations (Optional)
Transport information (Optional)
Regulatory information (Optional)
Other information

## Slide 38: How can you use an SDS?
Ingredients: Section 3
  What chemicals are in the product
  How much of each chemical is there
Chemical Hazards: Section 2
  Hazards associated with the chemical(s)
Safe Handling of Chemicals: Sections 7-8
  What Personal Protective Equipment (PPE) you should wear
  Other instructions on how to protect yourself

## Slide 39: Question
Which of the following pieces of information are found in an SDS?
  Ingredients
  Chemical hazards
  Safe handling of chemicals
  First-aid measures
  All of the above

## Slide 40: Question / Response 4
Which of the following pieces of information are found in an SDS?
  Ingredients
  Chemical hazards
  Safe handling of chemicals
  First-aid measures
  All of the above
Chart: 
| Ingredients | Chemical hazards | Safe handling of chemicals | First-aid measures | All of the above
004 | 0.5 | 0 | 0.5 | 0 | 0
Question / Response 4
10

## Slide 41: Answer 4

## Slide 42: Chemical hazards & GHS in oil & Gas

## Slide 43: types of Hazardous chemicals in oil & Gas
Acids
Volatile Organic Carbons (VOCs)
  Condensate, produced water, benzene
Toxic Gases
  Hydrogen sulfide
Naturally Occurring Radioactive Material (NORM)
Other Chemicals
  Silica
  Methanol
  Glycols (ethylene glycol, triethylene glycol)
  Heavy metals

## Slide 44: Acids
Corrosive/caustic chemicals
Irritants
Ways to protect yourself
  Skin protection – gloves & protective clothing
  Eye protection – goggles or face shield
Example:
  Hydrochloric Acid (HCl)

## Slide 45: Volatile organic compounds (VOCs)
Usually are flammable
Can cause acute and chronic health effects
Ways to protect yourself
  Skin protection – gloves & protective clothing
  Eye protection – goggles or face shield
  Respiratory protection – ventilation &/or respirator (chemical specific)
Examples:
  Produced water
  BTEX: benzene, toluene, ethylbenzene, xylene
  Petroleum distillates & condensate
  Petrochemicals

## Slide 46: Toxic gases
Can be flammable
Can cause acute health effects
Ways to protect yourself
  Monitor for gas (multi-gas meter)
  Ventilate area
  Respiratory protection – chemical specific respirator
Example:
  Hydrogen sulfide (sour gas) or benzene (sweet gas)

## Slide 47: Naturally Occurring Radioactive Material (NORM)
Potential for carcinogenic health effects
  Inhaled or ingested particles
Can be released from oil & gas formations
At-risk activities:
  Handling pipes or equipment contaminated with sludge, drilling mud, and pipe scale
  Cutting and reaming oilfield pipe
  Removing solids from tanks and pits
  Refurbishing gas processing equipment

## Slide 48: Other Chemicals – silica
Health hazards
  Cancer, lung, and kidney damage
Ways to protect yourself
  Ventilate area
  Respiratory protection – respirator (high efficiency particulate)

## Slide 49: Other Chemicals: Heavy Metals
Can be flammable in some forms
Can cause acute & chronic health effects
Ways to protect yourself
  Respiratory protection – ventilation &/or respirator (high efficiency dust, fume, mist)
  Practice good hygiene – wash hands & face before eating
  or drinking
Examples:
  Barium
  Cadmium
  Chromium
  Lead
  Mercury

## Slide 50: Other Chemicals: Methanol & Glycols
Can be flammable
Can cause acute and chronic health effects
Ways to protect yourself
  Skin protection – gloves & protective clothing
  Eye protection – goggles or face shield
  Respiratory protection – ventilation &/or respirator (chemical specific)

## Slide 51: Question / Response 5
You are working around a new chemical that can be inhaled. Which of the following pictograms would make you think about using a respirator?
A
B
C
D
Chart: 
| A | B | C | D
005 | 0 | 1 | 0 | 0
Question / Response 5
10

## Slide 52: Answer 5

## Slide 53: Questions?

## Slide 54: References & Resources
Oil & Gas Industry:
  OSHA. Oil and Gas Extraction. Accessed November 2017. Available at: https://www.osha.gov/SLTC/oilgaswelldrilling/index.html
  OSHA. Oil and Gas Well Drilling, Servicing and Storage—Storage Tanks. Accessed November 2017. Available at: https://www.osha.gov/SLTC/storagetank/index.html
GHS:
  UNECE. Globally harmonized System of Classification and Labelling of Chemicals (GHS). Seventh revised edition. Accessed November 2017. Available at: https://pubchem.ncbi.nlm.nih.gov/ghs/
  OSHA. Hazard Communication. Accessed November 2017. Available at: https://www.osha.gov/SLTC/oilgaswelldrilling/safetyhazards.html

## Slide 55: Training Post-assessment
How much do you already know about chemical hazards?
True or False:
  Hazard communication programs tell you about chemical hazards in your workplace.
  Hazard communication only tells about health hazards for a chemical.
  GHS is a system for classifying & labeling chemicals.
What are the ways a chemical can enter your body?