## Slide 1: Hazardous Materials Safety & Security Awareness Training Section III
Gathering and Analyzing Information

## Slide 2: Funding Acknowledgement
This material was produced under grant number SH-31200-SH7 from the Occupational Safety and Health Administration, U.S. Department of Labor. It does not necessarily reflect the views or policies of the U.S. Department of Labor, nor does mention of trade names, commercial products, or organizations imply endorsement by the U.S. Government.

## Slide 3: Section III Objectives
List six clues for hazardous materials/WMD recognition and identification
Recognize the appropriate U.N./DOT hazard class for various substances
Identify the product name using U.N. identification numbers
Recognize the general type of container, product and hazards that may be present in various types of transportation vessels

## Slide 4: Recognition and Identification Clues
Occupancy/Location
Container/Vehicle Shapes
Placards, Labels, and Markings
Non-Transportation Markings and Colors
Written resources, Safety Data Sheets
Senses

## Slide 5: Clue 1: Occupancy/Location
Type of occupancy at the incident scene
  Shipboard
  Dockside
  Warehouse
  Vehicle Type
  Type of Industry

## Slide 6: Clue 1: Occupancy/Location
Knowledge of the specific geographic area or transportation corridor
  Port
  Off shore facility
  Interstate highway
  Rail line
  Pipeline

## Slide 7: Clue 1: Occupancy/Location
All occupancies or locations have the potential to involve hazardous substances/WMD
Awareness
Vessel Emergency Plans
Facility Emergency Plans
Always consider hazardous substances may be present!

## Slide 8: Activity 3.1 Recognizing Occupancy and Location
Using the ERG, view the following slides and identify:
  Location
  Type of occupancy
    Property
    Life
  Material
  ERG page number
  Other useful information

## Slide 9: Activity 3.1: Example 1

## Slide 10: Activity 3.1: Example 2

## Slide 11: Activity 3.1: Example 3

## Slide 12: Activity 3.1: Example 4

## Slide 13: Activity 3.1: Example 5

## Slide 14: Activity 3.1: Example 6

## Slide 15: Activity 3.1: Example 7

## Slide 16: Ammonia Spill Video
WATCH ON YOU TUBE
https://www.youtube.com/watch?v=sNkdAs1e7Cw
Notes: Watch on You Tube

## Slide 17: Clue 2 :Container/Vehicle Shapes
Container characteristics can indicate content/hazard
  Shape
  Size
  Composition
  Transport vehicle type

## Slide 18: Transportation Modes
  Highway
  Railway
  Water
  Air
  Pipeline

## Slide 19: Highway Transportation
  Box trailer
  Flatbed
  Dry bulk
  Van
  Tube trailer
  Tank trailer
  Personal or company vehicle
  Approximately 50% of all highway transports are carrying hazardous materials
    Only 50% of these transports containing hazardous materials are required to display placards

## Slide 20: Box Trailer
  Typically mixed cargo
    bags
    boxes
    drums
    tanks
    cylinders
  Several placards or none
  Cargo not visible

## Slide 21: Flatbed
  Large Objects
  Bulk
  Non-bulk
  All classes of hazmat

## Slide 22: Dry Bulk Cargo Tank
  Carries solid materials
    Dusts
    Powder
    Pellets
  Guide 134
  Materials can be corrosives/oxidizers
  V or W shape on the bottom of trailer

## Slide 23: Tank Trailers
  Built to government specifications
    Motor Carrier (MC)
    Dept. of Transportation (DOT)
    Transport Canada (TC)
  Various tank truck diagrams in ERG

## Slide 24: Low Pressure Chemical Tank MC 306 / DOT 406
  Oval/Elliptical
  Aluminum construction with bottom piping
  Shell may be smooth or external ribs

## Slide 25: DOT 306 / 406 Compared to DOT 307 / 407

## Slide 26: High Pressure Tank MC 331
  Round cross section
    Liquefied petroleum gases
    Liquefied compressed gases
  Subject to “Boiling Liquid Expanding Vapor Explosion” (BLEVE)

## Slide 27: Cryogenic Liquid Tank MC 338
  Gases Transported as liquid
  Product name on each side of trailer
  Large bulky shell with heavy insulation
  Loading station in middle or end of trailed

## Slide 28: Tube Trailer
  Group of compressed gas cylinders
  Gases under high pressure
  Products carried include
    Helium/Oxygen/Hydrogen
    Refrigerant gases

## Slide 29: Personal or Company Vehicle
  Awareness.. Do not assume
  Items often transported
    Radioactive pharmaceuticals
    Industrial chemicals
    Household chemicals

## Slide 30: Railway Transportation
  Boxcar
  Flatcar
  Gondola
  Covered Hopper Car
  Open Hopper Car
  Low-Pressure Tank Car
  High Pressure Tank Car
  Cryogenic Tank Car
  Trailer on a Flat Car (TOFC)
  Container on a Flat Car (COFC)
  Intermodal Tank Car

## Slide 31: Box Car

## Slide 32: Covered Hopper Car

## Slide 33: Open Hopper Car

## Slide 34: Low-Pressure Tank Car
  Solids – sulfur, phosphorus
  Liquids – industrial solvents, motor fuels, food grade products
  May have 6 compartments
  Tank within a tank
    Outer shell holds insulation over an inner tank

## Slide 35: Low-Pressure Tank Car
  Non-pressure may not be accurate description
    Non-pressure may have up to 100 psi
  Man-way and fittings on top of car
  Carry solids that can be liquefied with heat for loading or unloading

## Slide 36: Pressure Tank Car
  Large, round protective housing on top contains all valves
  May carry liquefied compressed gases
    Poisons
    Oxidizers
    Asphyxiants
    Other combinations

## Slide 37: Pressure Tank Car
  Insulated or non insulated
  May have thermal protection coating sprayed on exterior
  May experience BLEVE if involved in fire

## Slide 38: Cryogenic Tank Car
  Tank within a tank
  Loading and unloading fittings underneath at the center or end of car
  Common products shipped
    Nitrogen
    Oxygen
    Carbon monoxide

## Slide 39: Intermodal (IM) Containers
  Highway to Rail to Water
  Carry any type of material
  Often affixed to railcars
  May be:
    Trailers
    Box like containers
    Tank supported by frame

## Slide 40: Intermodal (IM) Containers

## Slide 41: Water Transportation
  Ships and barges
  Large quantities of product
  Large problems during an incident

## Slide 42: River Port

## Slide 43: Tanker Ship

## Slide 44: Tanker Ship

## Slide 45: Coastal Trading Vessel

## Slide 46: Refrigerator “Reefer” Ship

## Slide 47: Heavy Lift Ships

## Slide 48: Cruise Ship

## Slide 49: Livestock Vessel

## Slide 50: Air Transportation
  Hazmats transported in dedicated cargo planes or passenger planes
  Heavily regulated
  Quantities limited by type of aircraft and chemical
  Aircraft carries large amounts of fuel
  Cargo aircraft uses containers called “Unit Load Device” (ULD)

## Slide 51: Cargo Plane

## Slide 52: Pipeline Transportation
  Below or above ground
  Carries variety of products
  Multiple products may be carried
  High pressures

## Slide 53: Pipeline Markers
  Indicate where line crosses or goes under water, roads, residential areas, etc.
  Pipeline rights of way are about 50ft wide

## Slide 54: Activity 3.2 Recognizing transportation containers
Using the ERG, view the following slides and identify:
  Location
  Type of occupancy
    Property
    Life
  Material
  ERG page number
  Other useful information

## Slide 55: Activity 3.2: Example 1

## Slide 56: Activity 3.2: Example 2

## Slide 57: Activity 3.2: Example 3

## Slide 58: Activity 3.2: Example 4

## Slide 59: Activity 3.2: Example 5

## Slide 60: Activity 3.2: Example 6

## Slide 61: Activity 3.2: Example 7

## Slide 62: Fixed-Site Containers
  Various different types of containers
  Potential for large quantities
  Can include transport containers
  Containers are classified by pressure
    Atmospheric: 0 - 5 psi
    Low pressure: 5 - 100 psi
    High pressure: 100 - 3,000 psi
    Ultra high-pressure: > 3,000 psi

## Slide 63: Atmospheric
  Contains liquids or solids
  Size range and configurations vary
  Multi-container packages common
  Above and below ground fuel storage tanks
  Types of packaging
    Bags
    Jars
    Boxes
    Totes
    Cans
    Drums
    Liquid Fuel Storage Tanks

## Slide 64: Individual Containers
  Smaller quantities
  Various sizes and shapes
  DOT labels affixed to packages for transportation
  Facility markings may be different on non-transport storage or usage

## Slide 65: Non-Bulk Bag

## Slide 66: Non-Bulk Containers
Drums
  Construction materials
    Fiberboard
    Metal
    Plastic
  Openings
    Open head, chime/bolt ring
    Tight or closed head, bung & inspection holes

## Slide 67: Non-Bulk Containers
Pressurized cylinders
  May hold
    Liquefied or non-liquefied gas
    Dissolved gases
    Solids or liquids
    Cryogenics

## Slide 68: Low Pressure
  Special Drums
  Equipment/processing
  Storage Tanks
  Pipelines
  Used for Volatile liquids, solids and some gases

## Slide 69: Horizontal Cylindrical Tank

## Slide 70: Covered Top Floating Roof Tank with Geodesic Dome

## Slide 71: High Pressure
  Cylinders and spheres
    Ex. Medical oxygen cylinders
  Normally contain gases, liquids or powders
  Usually above ground

## Slide 72: High-Pressure Spherical Tank

## Slide 73: High-Pressure Horizontal “Bullet” Tank

## Slide 74: Packaging of Radioactive Materials
  Packed and shipped under strict regulations
  Regulations designed to protect:
    Public
    Transportation workers
    Environment
  Packaging depends on form, type, and activity

## Slide 75: Types of Packaging
  Excepted
  Strong Tight
  Type A
  Type B

## Slide 76: Types of Packaging
Excepted
  For small amounts or radioactivity
  Typical shipping packages
  Not required to be labeled
  Examples:
    Smoke detectors
    Luminous watch dials
    Medical diagnostic kits

## Slide 77: Types of Packaging
Strong Tight
  Low Specific Activity (LSA) materials
  Materials from laboratories, power plants, and hospitals
  Type A packaging
    Labeled “RADIOACTIVE LSA”
    Danger is minimal

## Slide 78: Types of Packaging
Type A
  Greater amounts of activity
  Designed to hold contents in rough handling
  Amount is specified by radionuclide and form
  Examples
    Radiopharmaceuticals
    Industrial radiography sources
    Research sources

## Slide 79: Types of Packaging
Type B
  Highly radioactive
  No recorded failures during transportation
  Designed to hold contents under:
    Extreme accident conditions
    Submersion in water
    Puncture, fall, and thermal extremes

## Slide 80: Clue 3: Placards, Labels, and Markings
  Identify presence
  Identify dangers
  Identify products
  Not always uniform

## Slide 81: Placards
  10.75 inch diamond
  Color-coded
  Contain symbols
  Applied to sides and ends of containers
  Nine hazard classes, listed on Chart 15
    Table 1 (placard any quantity)
    Table 2 (placard 1,001 lbs. or more)

## Slide 82: Class 1: Explosives

## Slide 83: Class 2: Gasses

## Slide 84: Class 3: Flammable Liquids

## Slide 85: Class 4: Flammable Solids

## Slide 86: Class 5: Oxidizers

## Slide 87: Class 6: Toxic Materials

## Slide 88: Class 7: Radioactive Materials

## Slide 89: Class 9: Miscellaneous

## Slide 90: Class 9: Miscellaneous

## Slide 91: Marine Pollutant

## Slide 92: Dangerous Placard

## Slide 93: Labels
  4 inch square
  Scaled-down version of placards
  Used on individual packages
  Typically found in one or two locations on package
  Multiple products
    Primary label
    Subsidiary label for each hazard

## Slide 94: Clue 4: Non-Transportation Markings and Colors
  NFPA 704
  Hazard Communications
  Container Markings and Stencils
  Military Markings

## Slide 95: National Fire Protection Association (NFPA) 704
  Requirements for fixed-site locations
  Identifies hazards and dangers
  4-quadrant diamond
  Color and numeric identifiers

## Slide 96: NFPA 704 Diamond

## Slide 97: Hazard Communications
  Referred to as Hazardous Materials Information System (HMIS)
  Colored bars or diamonds
  Similar to NFPA 704
  Found on individual containers
  For normal work environments, not for emergencies

## Slide 98: Hazardous Materials Information System (HMIS)

## Slide 99: DOT HAZMAT Markings
  Hot Marking - used on elevated temperature products
  Marine Pollutant - products known to pollute water
  Inhalation Hazard – products that are poisonous when inhaled
  Infectious Substances - products that may affect public health (Class 6)

## Slide 100: Markings

## Slide 101: Railcar Stencils
  Reporting marks and number
    Left end when facing tank car
    Weight/volume
  DOT specifications
    Right end when facing tank car
    Tank material
    Test pressure/relief settings
    Product name (dedicated cars)
  Listed in ERG

## Slide 102: Tank Car Markings
Weight Limit
ABCX 123456
LD LMT 000000 lb 00000 kg
Car Initial & Number (reporting marks)
Specification Stencil
Water Capacity
Stencil
SAFETY VALVE 75 PSI TESTED 00/00/00 DUE 00/00/00 TANK 100 PSI DUE 00/00/00

## Slide 103: Reporting Rail & Intermodal Markings
  Markings can be thought of as “license plates”
  Shipping papers
  Locations
    Upper left on the side of railway cars
    Top center on railway tank heads
    Upper right on the sides and ends of intermodal containers

## Slide 104: Military Markings

## Slide 105: Activity 3.3 Recognizing Placards and Markings
Using the ERG, view the following slides and identify:
  Placard
  Class
  Material
  ERG page number
  Other useful information

## Slide 106: Activity 3.3: Example 1

## Slide 107: Activity 3.3: Example 2

## Slide 108: Activity 3.3: Example 3

## Slide 109: Activity 3.3: Example 4

## Slide 110: Activity 3.3: Example 5

## Slide 111: Activity 3.3: Example 6

## Slide 112: Clue 5: Written Resources
  Manifest/Shipping Papers
  Material Safety Data Sheets (MSDS)
  Safety Data Sheets (SDS) – GHS
  NIOSH

## Slide 113: Clue 5: Written Resources
DOT Required Description
  Proper shipping name
  Hazard class or division
  ID number
  Packing group
  Quantity

## Slide 114: Shipping Papers
  Each mode of transportation has a specific name and location for its manifest/shipping papers
  Person in charge of vessel/vehicle must maintain these papers
  Shipping paper details
    No abbreviations (unless DOT approved)
    Emergency response phone number
    Quantity of material
    Number of containers

## Slide 115: Types of Shipping Papers
Highway
  Name: Bill of Lading
  Location: Cab or driver
Railway
  Name: Consist or Waybill
  Location: Crew or engine
Waste
  Name: Hazardous Waste Manifest
  Location: Person in charge of vessel/vehicle
Water
  Name: Dangerous Cargo Manifest
  Location: Ship Captain, wheelhouse, or special container in barges
Air
  Name: Air Bill
  Location: Pilot or cockpit

## Slide 116: Safety Data Sheets
Material Safety Data Sheet (MSDS)
  Format not regulated by 29 CFR 1910.1200
  Style and content vary
Safety Data Sheet (SDS)
  Global Harmonization System (GHS)
  Format is regulated

## Slide 117: 16-Section Safety Data Sheet
Identification of the substance or mixture and of the supplier
Hazards identification
Composition/information on ingredients Substance/Mixture
First aid measures
Firefighting measures
Accidental release measures
Handling and storage
Exposure controls/personal protection
Physical and chemical properties
Stability and reactivity
Toxicological
Ecological information (non mandatory)
Disposal considerations (non mandatory)
Transport information (non mandatory)
Regulatory information (non mandatory)
Other information including information on preparation and revision of the SDS

## Slide 118: Locating Safety Data Sheets
  Required at fixed facilities
  Might be with shipping papers
  Shipper/Manufacturer
  CHEMTREC
  LEPC
  On-line or paper collections

## Slide 119: Clue 6: Senses
  Vision
    Colored clouds or fumes
    Containers that are dented, punctured, or on their side
  Hearing
    Sirens/alarms
    Chemical reactions occurring in containers (bubbles, popping, etc.)
  Smell
    Scent can be the first sign of a chemical leak/spill

## Slide 120: Summary
  Occupancy/Location
  Container/Vehicle Shapes
  Placards, Labels, and Markings
  Non-Transportation Markings and Colors
  Written resources, Safety Data Sheets
  Senses