## Slide 1
How would you like it if people drove their cars thru your office?

## Slide 2: Work Zone Safety
More than 40,000 people are injured each year as a result of motor vehicle crashes in work zones

## Slide 3: How serious is the WZ Problem?
835 fatalities
$4.4 billion Annual Cost
75 workers killed by vehicles/equipment
2007 Statistics

## Slide 4: How is Motorist Crash Risk Affected?

## Slide 5: Drowsy Driving in Work Zones

## Slide 6: Drunk Driving in Work Zones

## Slide 7: Highway Equipment Related Fatalities
Workers on Foot
57%
Operators
35%
Passengers
8%
Source: Bureau of Labor Statistics
Notes: Trainers Notes:
Most of the workers on foot are killed by being run-over by equipment, especially backing equipment. Some are killed by equipment tip-over or failure.
The most common cause of operator fatality is equipment roll-over. Many passengers are killed because they were not in a proper seat and were riding on steps, fenders, tailgates, buckets, etc., and fell off.

## Slide 8: Highway Worker Fatalities
Other
18%
Vehicle Entering
Work Area
22%
Construction Equipment
41%
Traffic Crash
19%
Source: Bureau of Labor Statistics
Notes: Trainers Notes:
Reinforce that the number one cause of highway worker fatalities is being killed by construction equipment.
Deaths from vehicles entering work areas are usually the result of driver error or improperly erected work zones.

## Slide 9: Work Zone Safety
Speed: the number one concern in work zone safety

## Slide 10: Work Zone Safety
Distracted Driving:
  Reaching/looking for items in the car
  Things, events outside of the car/rubbernecking
  Cell phones
  Adjusting the radio
  Eating
  Grooming
  Children and pets
Unsafe Condition

## Slide 12: What does WZ Safety mean to the public?

## Slide 13: Work Zone Safety
As a result of the Public’s Perception…
…the desired effect of our traffic control sometimes gets compromised.

## Slide 16: What does WZ safety mean to the contractor?

## Slide 19: Safety
Remember, there is only 1 goal
You, the motorist, bicyclist and the pedestrian must go home at the end of each work day.
There are no other acceptable alternatives.

## Slide 21: Traffic Issues
Sight Distance – Blind Curves
  Need extra signage
High Speed – High Traffic Volume
  No gaps for merging vehicles
  Stopping traffic is impractical and unsafe
Tailgating
  Motorists following trucks into work space
  Panic stops
The motorist NEEDS MORE information

## Slide 22: Work Zone Issues
Acceleration/Deceleration lanes
  Short or non-existent
Signage indicating merge/exit points
  Signs give vague information
  Messages left up 24/7
Flagging operations
  Works best with low traffic and moderate construction trucks
  Low construction truck traffic means intermittent flagging
    Proper rules are forgotten
Information must be accurate and REAL TIME!

## Slide 24: Work Zone Safety
Congestion on our roads is growing. Vehicle miles of travel are growing at a rate greater than mile of roadway:
Between 1982 and 2002, vehicle miles traveled increased by 79 percent, while highway lane miles only increased 3 percent during the same period.
(U.S. Department of transportation, Federal Highway Administration, Highway Statistics 2001, Publication No. FHWA-PL-02-020 Washington, DC , 2001.)

## Slide 25: Internal Work Zone Traffic Control for worker protection
Traffic cones from Europe
Not proper use of Jersey Barrier

## Slide 26: Additional Truck Mounted Attenuators (as needed for project)

## Slide 27: Additional Message Boards

## Slide 29: Backer Spotter

## Slide 30: Trucks – access and egress

## Slide 31: Additional Law Enforcement

## Slide 32: Making Worker more Visible

## Slide 33: Additional Warnings

## Slide 34: Additional Warnings

## Slide 35
CONES ARE ONLY APPROPRIATE AT SHORT TERM SITES

## Slide 36: Traffic Control Devices
Effective
Changeable message signs
Arrow panels
Warning flags and lights on signs
Effective buffer space
Trained flaggers and spotters

## Slide 37: Other TCDs & Safety Devices
Enhanced flagger setups
Intrusion alarms
Rumble strips
Pace or pilot vehicle
High quality work zone pavement markings and removal of misleading markings
Reduced channelizing device spacing

## Slide 38: Good TTC Achieves Multiple Goals
Movement of vehicles, bicycles, pedestrians
Accommodates transit operations
Provides access to property and utilities
Protects workers and work operations
Allows efficient completion of the work
Bottom line = reasonably safe & efficient movement of road users while protecting workers & completing work efficiently

## Slide 39: What is an Internal Traffic Control Plan?
Developed by the contractor
Coordinates vehicle and equipment movement inside the work zone
Limits exposure of workers on foot to construction traffic
Reduce hazards for equipment operators

## Slide 41: “Stage” the Roadway Work Zone
Advance Warning
Transition
Activity – Work space, Buffer space, Traffic space
Termination

## Slide 42: Work Zone Safety
Traffic control plan is needed
Traffic control devices must be used inside the work zone
First warning should be 4-8 times (in feet) the speed limit (in mph)
Flaggers and others need high visibility, reflective clothing and training
Notes: Trainers Notes:
OSHA makes the following recommendations:
Give motorists plenty of warning of upcoming work zones; place the first warning signs at a distance calculated as 4 to 8 times (in feet) the speed limit (in mph)-use a higher multiplier for higher speed areas (e.g., a 15 mph road should have its first warning sign at least 60 feet from the work zone, while a work zone needed in a 65 MPH zone should have its first sign approximately 520 feet away).
Work zone safety requires:
Traffic control plan is needed
Traffic control devices must be used inside the work zone
First warning should be 4-8 times (in feet) the speed limit (in mph)
Flaggers and others need high visibility, reflective clothing and training

## Slide 43: Principles of Safe Traffic Control
Plan for Safety
Keep if Moving
Communicate
Monitor
Plan for the Worst
Train

## Slide 44: The Future of Work Zones
It is possible to reduce work zone accidents
Goals:
  Indentify and create best practices
  Implement Internal Traffic Control strategies for improved motorist information on destination and delay

## Slide 45: Considerations
Pre-shift meeting with all involved
Everyone must know what is happening for the day.

## Slide 46: Work Zone Safety
However…
“The owner would not always allow us to place additional safety devices on the job!”
“We did not get paid for a lot of those extra safety devices!”