## Slide 1: Powered Industrial Trucks

## Slide 2: Disclaimer
Powered Industrial trucks
This material was produced under
grant number SH-05073-SH8 from the Occupational Safety and Health Administration, U.S. Department of Labor.
It does not necessarily reflect the views or policies of the U.S. Department of Labor, nor does mention of trade names, commercial products, or organizations imply endorsement by the U.S. Government.

## Slide 3: Welcome
Powered Industrial trucks
P.I.T. Types & How they work
Pre start Inspection
Driving Safety
Maintenance

## Slide 4: Module-1
Powered Industrial trucks
P.I.T. Types & How they work
Pre-Start Inspection
Driving Safety
Maintenance

## Slide 5: Typical Forklift
Powered Industrial trucks

## Slide 6: Stand-On Reach Truck
Powered Industrial trucks

## Slide 7: Walkie Rider
Powered Industrial trucks

## Slide 8: How they Work
Powered Industrial trucks
Steering Your Forklift
Isn’t as Simple as
Turning the Wheel

## Slide 9: How they Work – Part 2
Powered Industrial trucks
Steering Your Forklift Isn’t as Simple as Turning the Wheel
Many accidents occur with industrial forklifts because the operators do not understand or have control of the machine’s rear end swing.
Forklift trucks steer from the rear axle and pivot on the front wheels, the rear end (counterweight) swinging wide when turning. Ensure that the rear end swings clear of materials, racks equipment and pedestrians when rounding corners or maneuvering in aisle and tight places.

## Slide 10: How they Work – Part 3
Powered Industrial trucks
Don’t expect a forklift to handle like a car or truck.
Because of the counterweight over its rear wheels, a forklift is much heavier than a car. As a result, it can’t stop or turn quickly.
When turning a forklift, watch behind you to make sure the rear end of the lift doesn’t run into anything – or anyone. Also keep an eye out for your forks and any load you may be carrying.
Most forklifts have a three-point suspension system. The three points are the two front wheels and the pivot point of the rear axle. Connect the three points, and you have what’s called the stability triangle.

## Slide 11: How they Work – Part 4
Powered Industrial trucks
FULCRUM
Point

## Slide 12: How they Work – Part 5
Powered Industrial trucks
FULCRUM
Point

## Slide 13: How they Work – Part 6
Powered Industrial trucks
Capacity and
Load Centers

## Slide 14: How they Work – Part 7
Powered Industrial trucks
Capacity and
Load Centers

## Slide 15: How they Work – Part 8
Powered Industrial trucks

## Slide 16: Rated Capacity
Powered Industrial trucks

## Slide 17: Rated Capacity – Part 2
Powered Industrial trucks

## Slide 18: Module-2
Powered Industrial trucks
P.I.T. Types & How they work
Pre-Start Inspection
Driving Safety
Maintenance

## Slide 19: Pre-Start Inspection
Powered Industrial trucks
It is necessary to inspect the work site also. Items to inspect include:
The surface on which the Forklift will be used,
Hazards that might create dangerous driving conditions,
Above hazards that may effect personal while the Forklift is extended,
Weather conditions

## Slide 20: Pre-Start Inspection – Part 2
Powered Industrial trucks
Visual Inspection
  Appearance * Tires
  Forks * Overhead Guard
  Hoses * Chain
  Name Plate * Leaks
  Battery Connector * Battery Cables

## Slide 21: Pre-Start Inspection – Part 3
Powered Industrial trucks
Forklift Nameplate:
Basics A forklift's nameplate (also referred to
as a data plate, weight plate or load plate)
Provides integral information about the machine's capacity, fuel type, and weight.
Workers and operators can refer to the nameplate to ensure safe and efficient operation.

## Slide 22: Pre-Start Inspection – Part 4
Powered Industrial trucks
Tires –
What are they generally made of?
Are they Damaged?

## Slide 23: Pre-Start Inspection – Part 5
Powered Industrial trucks
Forks –
What are we looking for?
Why?

## Slide 24: Pre-Start Inspection – Part 6
Powered Industrial trucks
Hydraulics –
Leaks?
Parking area?

## Slide 25: Pre-Start Inspection – Part 7
Powered Industrial trucks
Hydraulics –
Leaks?
Parking area?

## Slide 26: Pre-Start Inspection – Part 8
Powered Industrial trucks
Mast –
Cracks?
Broken or Elongated links?

## Slide 27: Pre-Start Inspection – Part 9
Powered Industrial trucks
Operating Checks
  Horn * Seat/Belt
  Hour Meter * Overhead Guard
  Battery Indicator * All Lights
  Back-up Alarm * Mirror
  Gauges

## Slide 28: Module-3
Powered Industrial trucks
P.I.T. Types & How they work
Pre-Start Inspection
Driving Safety
Maintenance

## Slide 29: Driving Safety
Powered Industrial trucks
Authorized operators only
Quickly report accidents
Always wear seat belts
No person under the forks
Operate controls only from driver’s seat
Never block exits or emergency equipment

## Slide 30: Driving Safety – Part 2
Powered Industrial trucks
Loading and Unloading
  Never overload forklift
  Check load weight
    Locate load’s center of gravity
  Inspect the load
  Restack or secure unstable loads
  Be sure forks are under load
  Tow from rear towing pin

## Slide 31: Driving Safety – Part 3
Powered Industrial trucks
Traveling
  Look in the direction of travel
  Keep body inside cage
  Keep forks low when traveling
  Sound the horn
  Don’t speed
  Check clearance

## Slide 32: Driving Safety – Part 4
Powered Industrial trucks
  Avoid loose objects or holes
  Never carry passengers
  Pedestrians have the right-of-way
  Keep a safe distance from the edge of ramps or docks
  Never eat or drink
  No horseplay
Traveling

## Slide 33: Driving Safety – Part 5
Powered Industrial trucks
  Inspect the dock plate
  Check the trailer floor condition
  Make sure trailer wheels are chocked
  Ensure that the nose of the trailer is supported by the tractor or safety stabilizer.
Loading Docks

## Slide 34: Driving Safety – Part 6
Powered Industrial trucks
  Inspect the dock plate
  Check the trailer floor condition
  Make sure trailer wheels are chocked
  Ensure that the nose of the trailer is supported by the tractor or safety stabilizer.
Loading Docks

## Slide 35: Driving Safety – Part 7
Powered Industrial trucks
  Don’t block exits or aisles
  Lower the forks
  Set gear to neutral
  Set the parking brake
  Turn off the ignition
Parking

## Slide 36: Don’t leave a forklift unattended.
Powered Industrial trucks
  A forklift is considered "unattended" when the operator is 25 ft. or more away from the vehicle even if it remains in his view, or whenever the operator leaves the vehicle and it is not in his view.
  When a forklift is left unattended, forks must be fully lowered, controls neutralized, power shut off, and brakes set.
  Wheels must be blocked if the truck is parked on an incline.

## Slide 37: Don’t leave a forklift unattended. – Part 2
Powered Industrial trucks
  A forklift is considered "unattended" when the operator is 25 ft. or more away from the vehicle even if it remains in his view, or whenever the operator leaves the vehicle and it is not in his view.
  When a forklift is left unattended, forks must be fully lowered, controls neutralized, power shut off, and brakes set.
  Wheels must be blocked if the truck is parked on an incline.
When the operator of a forklift is within 25 ft. of the truck still in his view, the load engaging means must be fully lowered, controls neutralized, and the brakes set to prevent movement, but the power does not need to be shut off.

## Slide 38: What to do in case of a tipover
Powered Industrial trucks
  If the forklift tips, keep your arms and legs inside and hold on to the steering wheel.
  Don’t attempt to jump out – you can’t move faster than the forklift can tip over. Most people who attempt to jump are killed by the impact of the overhead guard.

## Slide 39: Don’t travel with a raised load
Powered Industrial trucks

## Slide 40: Seatbelts
Powered Industrial trucks
  Seatbelts are required on all forklifts manufactured since 1992 and can be retrofitted on all older models.
  You are required to uses it when it is supplied with the forklift. It will save your life.
Buckle Up - Before you drive!!

## Slide 41: Proper loading of the fork truck:
Powered Industrial trucks
  Adjust the forks to distribute the weight evenly. Note that forks are adjustable.
  Tilt the mast back carefully to stabilize the load.
  Do not attempt to physically move or push a fallen or misaligned load back onto the forks. ensure that the forks do not go through to the other side where pallets are closely stacked.

## Slide 42: Forklift Do’s And Don'ts
Powered Industrial trucks
No one else on the forklift except the operator, unless the forklift has a seat for a rider.
Always drive with the forks lowered and lower forks to floor when parking the forklift.
No Speeding - Speed Limit not to exceed 6 MPH.
  No faster than a brisk walk

## Slide 43: Proper loading of the fork truck:
Powered Industrial trucks
  Adjust the forks to distribute the weight evenly. Note that forks are adjustable.
  Tilt the mast back carefully to stabilize the load.
  Do not attempt to physically move or push a fallen or misaligned load back onto the forks. ensure that the forks do not go through to the other side where pallets are closely stacked.

## Slide 44: Module-4
Powered Industrial trucks
P.I.T. Types & How they work
Pre-Start Inspection
Driving Safety
Maintenance

## Slide 45: Forklift Inspection and Maintenance
Powered Industrial trucks
All forklifts be examined at least daily before being used. Forklifts used on a round-the-clock basis must be examined at the start of each shift.
Check the following:
  Fluid levels -- oil, water, and hydraulic fluid.
  Leaks, cracks or other visible defect in hydraulic hoses and mast chains.
  Safety decals and nameplates in place and legible.
  All safety devices working properly including the seat belt and backup alarm.

## Slide 46: Trained and Authorized Operators
Powered Industrial trucks
Only operate Forklifts if trained and Authorized
Understand Operating Instructions and Safety rules.
Receive Hands-on Training from a Qualified Person.
Know how to Inspect Equipment and Work Area.
Demonstrate How to Safely Operate Equipment.
Keep at Least 10 feet Away from Power Lines.
Never disable a safety or warning device.

## Slide 47: Review
Powered Industrial trucks

## Slide 48: Knowledge Check
What are the three basic types of Powered Industrial Trucks?

## Slide 49: Knowledge Check – Part 2
What are the three basic types of Powered Industrial Trucks?
    Standard Sit-down Forklift
    Reach Truck
    Walkie-Rider

## Slide 50: Knowledge Check – Part 3
Forklifts turn on which axle?

## Slide 51: Knowledge Check – Part 4
Forklifts turn on which axle?
Powered Industrial Trucks turn with their rear wheels and pivot on the front wheels, the rear end swings wide. The operator must develop the habit of allowing room for this in order to avoid hitting anything.

## Slide 52: Knowledge Check – Part 5
What is the Fulcrum point?

## Slide 53: Knowledge Check – Part 6
What is the Fulcrum point?

## Slide 54: Knowledge Check – Part 7
4. A visual Inspection should include….?

## Slide 55: Knowledge Check – Part 8
4. A visual Inspection should include….?
Visual Inspection
  Appearance * Tires
  Forks * Overhead Guard
  Hoses * Chain
  Name Plate
  Battery Connector * Battery Cables
  Leaks

## Slide 56: Knowledge Check – Part 9
5. When is a Forklift considered . UNATTENDED?

## Slide 57: Knowledge Check – Part 10
5. When is a Forklift considered . UNATTENDED?
  A forklift is considered "unattended" when the operator is 25 ft. or more away from the vehicle even if it remains in his view, or
  whenever the operator leaves the vehicle and it is not in his view.

## Slide 58: Additional Resources
OSHA website: http://www.osha.gov and OSHA offices: Call or Write (800-321-OSHA)
Compliance Assistance Specialists in the area offices
National Institute for Occupational Safety and Health (NIOSH) – OSHA’s sister agency
OSHA Training Institute Education Centers
Standards that Apply OSHA Standards: 29 CFR 1910.67, 29 CFR 1910.269(p), 29 CFR 1926.21, 29 CFR 1926.453, 29 CFR 1926.502. American National Standards Institutes standards: ANSI/SIA A92.2-1969, ANSI/SIA A92.3, ANSI/SIA A92.5, ANSI/SIA A92.6.