## Slide 1: Silica in Construction
A training to
keep construction workers safe on the job
State Building & Construction Trades Council of California,
AFL-CIO
Funded by Federal OSHA, 2017

## Slide 2: Funded by OSHA
This material was produced under grant SH29642SH6 from the Occupational Safety and Health Administration, U.S. Department of Labor. It does not necessarily reflect the views or policies of the U.S. Department of Labor, nor does mention of trade names, commercial products, or organizations imply endorsement by the U.S. Government

## Slide 3: Use of Material Duplication and Photo Credit
Material is only to be used for non-commercial, instructional, educational purposes
Fees may not be charged for this material
Photo credits are given on each slide
While every effort has been made to ensure information is current and accurate, the SBCTC does not assume any liability for errors or omissions

## Slide 4: Acknowledgements
We thank the following organizations for:
Providing technical assistance with developing this training:
  Center for Construction Research and Training (CPWR)
  UC Berkeley Labor Occupational Health Program (LOHP)
  Cal/OSHA
  Federal OSHA
Sharing: photos, video, training material
  BAC –International Union of Bricklayers and Allied Crafts
  CA Dept. of Industrial Relations—Commission on Health and Safety and Workers’ Compensation (WOSHTEP program)
  West Virginia Archives
  Worksafe BC (Canada)

## Slide 5: Silica—A High Priority for Construction
2 million U.S. construction workers exposed to silica every year
eLCOSH images
Notes: Photo: Scarifying concrete, no controls being used to reduce exposure level.

## Slide 6: Course Objectives for Silica Training By the end of this training, participants will be able to:
Understand what it is
Recognize hazards
Describe health effects
Identify controls:
Engineering/work practice/PPE
Understand new OSHA Standard
Work safely around silica

## Slide 7: Section 1 Introduction to Silica
eLCOSH images
Notes: Photo: Demolition of Morris Mechanic theater Baltimore, MD, January 2015

## Slide 8: What is silica?
One of the most common minerals on Earth
Photos courtesy PDPhoto.org

## Slide 9: Mineral means:
Naturally occurring
Inorganic—not plant or animal
Solid form
Definite chemical composition

## Slide 10: Silica is found in rock, soil and sand
Silica is composed of the elements Silicon + Oxygen = SiO2
Photo: CPWR
Photo courtesy PDPhoto.org
eLCOSH images

## Slide 11: Silica naturally occurs as:
Amorphous: no regular form
Crystalline: well-defined arrangement, regular crystal form
Photo: CPWR
Which is hazardous?

## Slide 12: 3 forms of crystalline silica
Quartz—common,
found in sand, gravel, clay,
granite, sandstone and
other rock
Cristobalite and Tridymite—
less common, but more toxic to workers
Photo: CPWR

## Slide 13: Where is silica found in construction?
BRAINSTORM ACTIVITY
Based on what you just learned about
where silica naturally occurs, list the
building materials you think might contain
crystalline silica?

## Slide 14: These materials may contain silica
Asphalt
Brick
Cement
Concrete
Concrete block
Drywall
Fiber cement products (siding, cladding panels)
Grout
Gunite/Shotcrete
Mortar
Paints
Plaster
Refractory Mortar/Castables
Refractory units
Rock
Roof tile (concrete)
Sand
Soil (fill dirt, top soil, soil w/fly ash added)
Stone (granite, limestone, quartzite, sandstone, shale, slate, cultured, etc.)
Stucco/EIFS
Terrazzo
Tile (clay and ceramic)

## Slide 15: How can you find out if material contains silica?
Product label
Safety Data Sheet
Published data—online
Analyze a sample of the material
wikimedia

## Slide 16: Websites that can help you
CPWR (Center for Construction Research and Training) Work Safely With Silica
www.silica-safe.org
Federal OSHA Silica eTool
http://www.osha.gov/dsg/etools/silica
Cal/OSHA Silica in Construction eTool
http://www.dir.ca.gov/dosh/etools/08-019/index.htm

## Slide 17: Section 1 Review and Questions
Name three important things you learned in this section.

## Slide 18: Section 2 Silica As a Hazard
How does silica become a
construction hazard?

## Slide 19: Factors that determine potential to cause harm:
  Route of exposure
  Toxicity
  Dose and duration
  Interaction
  Individual characteristics

## Slide 20: Route of Exposure How does silica get into your body?
Breathing
eLCOSH images
Notes: Photo: Potential silica exposure to heavy equipment operators. (NIOSH/John Rekus)

## Slide 21: Size matters!
“Respirable” silica is small enough to penetrate body’s natural defenses and get deep into your lungs
Crystalline Silica
Photo source: CDC
It’s 100 times smaller than ordinary beach sand
wikimedia

## Slide 22: Respirable Particles
A single human hair is between
80 – 120 microns (µm) in diameter
Respirable dust is less than 10 microns (µm) in diameter
Slide courtesy of Construction Safety Council, Illinois

## Slide 23: Respirable Particles in Constructions

## Slide 24: Toxicity

## Slide 25: Dose and Duration
Amount of substance entering body
Amount of time you are exposed

## Slide 26: How much silica dust is too much? 3 Important terms:
TWA
AL
PEL
Time weighted average
Action Level
Permissible exposure limit

## Slide 27: New limits for silica
AL = 25 micrograms per cubic meter of air
(25 µg/m3) calculated as 8-hour TWA
PEL = 50 micrograms per cubic meter of air
(50 µg/m3) averaged over an 8-hour day

## Slide 28: What is a “microgram (µg) ”
A metric unit of weight or mass equal to
1 millionth of a gram
0.000001 g
Too small to see with the naked eye

## Slide 29: Pennies and Dollars

## Slide 30: Cubic Meter

## Slide 31: Interactions
Some substances, in combination, will increase the chance a worker will get sick.
Individual Characteristics
Age, gender, diet, state of health, pregnancy, use of medication, drugs and alcohol can change toxic effects

## Slide 32: Putting it all together Silica is hazardous because:
Causes lung disease, cancer, even death
Silica dust travels deep into your lungs
Short-time exposure to large amounts
causes harm
Airborne particles too small to see
Long-time exposure to small amounts causes harm
Found in many construction materials
Effects worse if you also smoke
eLCOSH images
Notes: Photo: Uncontrolled dust/silica exposure for operator and any workers in the immediate area. (NIOSH/John Rekus)

## Slide 33: Section 2 Review and Questions
Name three important things you learned in this section.

## Slide 34: Section 3 Tasks and Tools that Create Silica Dust
Top photos: Cal/OSHA
Photo: OSHA
Photo source: elcosh

## Slide 35: It’s dusty work… but somebody has to do it
SMALL GROUP ACTIVITY
Look at the list of construction materials that contain silica.
What kind of work do you do with these materials that may create dust?

## Slide 36: Operations that create silica dust
Cutting, drilling, coring
Grinding, sanding, sandblasting
Pulverizing
Mixing (dry)
Cleaning up
eLCOSH Images

## Slide 37: Group Discussion
Which phases of construction create the highest exposure to silica dust?
Can you think of any crafts that are never exposed to silica dust?

## Slide 38: Tasks with high chance of exposure
The probability (in %) of being overexposed
Based on PEL of 0.1 mg/m3
Notes: Based on a summary of University of Washington studies.

## Slide 39: “It wasn’t me!”
Workers who are not “engaged” in the task but are working nearby may be exposed to silica hazards.
May be covered by Multi-Employer Worksite regulations (OSHA)
“Creating”
“Exposing”
“Controlling”
“Correcting”

## Slide 40: The 5 question test
Did your employer:
1. Create the hazard?
2. Have responsibility or authority to correct hazard?
3. Have ability to correct or remove the hazard?
4. Demonstrate that creating, controlling and/or correcting employers were notified/aware of hazards?
5. Take appropriate feasible steps to protect their employees from the hazard, instruct them to recognize the hazard and inform how to avoid associated dangers?

## Slide 41: Section 3 Review and Questions
Name three important things you learned in this section.

## Slide 42: Section 4 Health Effects of Silica Exposure
Courtesy of: CPWR SmartMark

## Slide 43: Group Discussion
Do you know someone who has?
Have you personally experienced health effects from breathing silica dust?

## Slide 44: Breathing crystalline silica puts you at risk for serious, life-threatening disease
Photo: elCOSH images
Notes: Photo: Workers using respiratory protection to reduce exposure to silica dust. (Mount Sinai/CHEP)

## Slide 45: Which body part is most affected?
Lungs
More than 6 million breaths per year

## Slide 46: Respirable crystalline silica causes:
Silicosis—a serious lung disease
Lung cancer–classified as a carcinogen
Chronic obstructive pulmonary disease

## Slide 47: And contributes to:
Heart
disease
Kidney disease
Vascular
disease
Autoimmune
disease
Tuberculosis (TB)
and other infections

## Slide 48: Watch video:
Silica Exposure
by Worksafe BC http://www.youtube.com/watch?v=R_sC2wX9Uwc

## Slide 49: Silicosis Facts
Permanent
Irreversible
No cure
Worsens after exposure ends
Deadly
Preventing exposure is your best defense

## Slide 50: 3 types of silicosis:
Chronic
Acute
Accelerated
Normal Lung
Silicotic Lung

## Slide 51: Silica Table

## Slide 52: Silicosis signs and symptoms

## Slide 53: Workers speak up
Bricklayer stories of what it’s like to live with silicosis.
Play audio
Notes: Photo source: Construction Safety Council , Illinois—Harwood grant material

## Slide 54: Silicosis: One of oldest occupational diseases
Documented in 1700’s
Chronic effects tied to crafts
Increased with use of new power tools
Photo: wikimedia

## Slide 55: Hawk’s Nest Tragedy
1930’s Tunneling project through rock containing 96-99% silica
Few records kept but
historians now believe 2000-2500 workers contracted silicosis and over 700 died.
Photo: Google images

## Slide 56: West Virginia State Archives
Photo courtesy of: Elkem Metals Collection, West Virginia State Archives

## Slide 57: Impact of Hawk’s Nest
Revealed “Acute” silicosis
Directly connected exposure and illness
Spurred public outcry and increased demands for worker protection

## Slide 58: Watch video:
“Silica in Construction:
From danger to safety”
SBCTC

## Slide 59: Section 4 Review and Questions
Name three important things you learned in this section.

## Slide 60: Section 5 Controlling Silica Hazards
Photo source: elcosh
Notes: Photo: Unsafe work practice—scarifying concrete without dust controls. (Mount Sinai/CHEP)

## Slide 61: Your experience on-the-job
BRAINSTORM ACTIVITY
List all actions you’ve used to control silica.

## Slide 62: Hierarchy of Controls

## Slide 63: Assessing risk—factors to consider
What tool is being used?
What is silica content of material?
How enclosed is work area?
Is dusty work constant or intermittent?
Does the job take the whole shift?
Which control methods most effective <PEL?
Will PPE also be needed to meet the PEL?

## Slide 64: Engineering controls
Wet methods
Local exhaust ventilation (LEV)
Substitution
Isolation

## Slide 65: Examples of wet methods
Concrete/masonry saws that provide water to blade
Water hose to wet down dust at point of generation
During rock drilling, flow water through drill stem
Photos: CPWR Silica Safe

## Slide 66: Silica Dust while working
Photos: CPWR Silica Safe

## Slide 67: Silica Dust while working
Photos: CPWR Silica Safe

## Slide 68: Examples of LEV methods
Vacuum system captures dust close to source
Integrate systems onto equipment that generates dust
Use HEPA (high-efficiency particulate air) filter
Photos: CPWR Silica Safe

## Slide 69: Silica in Construction
Photos: CPWR Silica Safe

## Slide 70: Examples of control combinations
Asphalt pavement milling machines use ventilation and water-spray controls

## Slide 71: Silica at outdoor work places
Photos: CPWR Silica Safe

## Slide 72: Are controls working?
Follow manufacturer’s instructions/specifications
Use tools properly
Do required maintenance and cleaning regularly
Test the air for contaminants

## Slide 73: Air monitoring
Done by professionals
Identifies/ quantifies contaminants
Specialized, calibrated equipment
Personal monitoring of workers
General ambient air monitoring

## Slide 74: Air sampling equipment
Personal Air Pump with Cyclone

## Slide 75: Personal Monitoring
Determines individual worker exposure
Done during a specific time period
Pump pulls air through a filter or tube, which traps the dust or toxin.
Slide courtesy of Construction Safety Council, Illinois
Notes: Slide Credit: Construction Safety Council Harwood grant number SH-19495-09-60-F-17

## Slide 76: Examples of substitution
Eliminate the hazard
Use silica-free materials when feasible
Paints/coatings
Abrasive blasting
Steel shot
Corn cob
Coal slag
Garnet

## Slide 77: Examples of isolation
Separate the worker from the dust
Enclosed cab with ventilation/filtered air
Separate dusty operations from non-dusty areas
Abrasive blasting containment
Photo: eLCOSH Images

## Slide 78: Administrative controls
OSHA standard
Written plan
Job/task planning
Air monitoring
Training
Best work practices
Photo source: elcosh

## Slide 79: Best practices for contractors
Use controls to eliminate dust
Assign competent person
Provide proper respirators when needed
Substitute materials
Create a plan
Photo source: elcosh

## Slide 80: Best practices for workers
Use equipment and controls properly
Be aware
Participate
Don’t bring dust home
Give your doctor silica info
Don’t eat, drink, smoke, or apply cosmetics while near silica dust—wash hands/face
Photo source: elcosh

## Slide 81: Personal protective equipment
Only if engineering and work practice controls aren’t enough
Must be NIOSH approved
Employers must comply with OSHA silica and respiratory protection standards
Medical evaluations

## Slide 82: NIOSH-Approved Respirators
PAPR
N 95
½ face APR
Slide Courtesy of CPWR
Full Face APR

## Slide 83: Why is PPE less effective than engineering controls?
Doesn’t eliminate hazard
Can be uncomfortable
Hard to communicate
Limited vision/movement
Workers must know how to use properly
Difficult to maintain
Photo source: elcosh
Notes: Photo: Hazardous waste worker, operating real time gas monitor. Worker wearing level B protective equipment. (NIOSH/John Rekus)

## Slide 84: Watch video:
Eliminate the Hazard:
McCarthy Drilling Project
By: SBCTC
DISCLAIMER: This is a case study that illustrates the implementation of engineering controls for silica dust and is for educational purposes only. References to a specific employer or brand of equipment do not imply endorsement by either OSHA or the SBCTC and its affiliates.

## Slide 85: Section 5 Review and Questions
Name three important things you learned in this section.

## Slide 86: Section 6 The New OSHA Standard

## Slide 87: New Federal Silica Standard
Final rule published by OSHA—March 25, 2016
Timeline courtesy of the International Union of Bricklayers and Allied Craftworkers

## Slide 88: Scope of Coverage
Quartz, cristobalite and tridymite
All occupational exposures to respirable crystalline silica in construction work unless below Action Level
Photo source: elcosh
Notes: Photo: Unsafe work practices, no controls for silica exposure. (Earl Dotter.com)

## Slide 89: Compliance Date
Construction employers must comply with all requirements by June 23, 2017
(except requirements for laboratory evaluation of exposure samples, which begin June 23, 2018)

## Slide 90: What does the new standard do?
AL trigger
Lower PEL
Engineering controls and work practices to limit exposure
25 µg/m3 (8-hr TWA)
50 µg/m3 (8-hr TWA)

## Slide 91: What does the new standard do?

## Slide 92: What is “Table 1”
Matches 18 tasks with effective dust control methods and respirator requirements

## Slide 93: Table 1 Tasks/Equipment
Stationary masonry saws
Handheld power saws
Handheld power saws for fiber cement board
Walk-behind saws
Drivable saws
Rig-mounted core saws or drills
Handheld and stand-mounted drills
Dowel drilling rigs for concrete
Vehicle-mounted drilling rigs for rock and concrete
Jackhammers and handheld powered chipping tools

## Slide 94: Table 1 Tasks/Equipment con’t
Handheld grinders for mortar removal (tuckpointing)
Handheld grinders for other than mortar removal
Walk-behind milling machines and floor grinders
Small drivable milling machines
Large drivable milling machines
Crushing machines
Heavy equipment and utility vehicles to abrade or fracture silica materials
Heavy equipment and utility vehicles for grading and excavating

## Slide 95: Must fully/properly implement controls
Presence of controls not sufficient
Employers required to ensure:
  Controls present and maintained
  Employees understand/use properly

## Slide 96: Option 2: Alternative Exposure Control
If employers do not follow Table 1, they must comply with section (d) of the standard

## Slide 97: Section (d) requires:
Action Level and PEL apply
Must do exposure assessment using either:
  Performance option
  Scheduled monitoring option
Use engineering and work practice controls

## Slide 98: OSHA Compliance Guides for Silica
Available from OSHA website
https://www.osha.gov/Publications/OSHA3902.pdf

## Slide 99: All employers must comply with these sections of new standard:
Housekeeping
Medical surveillance
Recordkeeping
Haz Comm &
training
Create written plan

## Slide 100: Housekeeping: workers need to know
If contributes to silica exposure:
--Dry sweeping or brushing
--Use of compressed air for cleaning surfaces or clothing
NOT allowed unless used with ventilation
Photo source: elcosh

## Slide 101: Employers must have written plan for managing silica exposure
Available to each employee
Describes tasks, controls, PPE, procedures, housekeeping, restricted access to work areas
Designates a Competent Person

## Slide 102: Duties of competent person
Identify existing and foreseeable hazards
Authority to take prompt corrective measures
Frequently/regularly inspect job sites, material and equipment
Photo source: elcosh

## Slide 103: Medical exam available at no cost
If you wear a respirator 30 or more days/year for silica exposure
Exam includes:
-Medical/work history
-Physical exam
-Chest x-ray
-Pulmonary function test
-Tuberculosis test
Photo: wikimedia

## Slide 104: Exam results within 30 days
Physician provides the following written reports:
To employee—medical report
To employer—medical opinion

## Slide 105: Hazard communication and training Workers must have:
Access to:
Labels on material containers
Safety Data Sheets
And receive:
Hazard information
Training
Photo source: elcosh

## Slide 106: Section 6 Review and Questions
Name three important things you learned in this section.

## Slide 107: Review Game

## Slide 108: Work safely with silica and enjoy a healthy career in the trades
Photo source: elcosh
Thank you for attending this training.