## Slide 1: Ladder Safety Training
This material was produced under grant number SH-17787-08 from the Occupational Safety and Health Administration, U.S. Department of Labor. It does not necessarily reflect the views or policies of the U.S. Department of Labor, nor does mention of trade names, commercial products, or organizations imply endorsement by the U.S. Government. Revisions were made to this material under grant number SH-05059-SH8 from the Occupational Safety and Health Administration, U.S. Department of Labor.
Notes: Introduce yourself and welcome everyone to Central Georgia Technical College’s Ladder Safety Training.

## Slide 2: Disclaimer
This material was produced under grant number SH-17787-08 from the Occupational Safety and Health Administration, U.S. Department of Labor. It does not necessarily reflect the views or policies of the U.S. Department of Labor, nor does mention of trade names, commercial products, or organizations imply endorsement by the U.S. Government. Revisions were made to this material under grant number SH-05059-SH8 from the Occupational Safety and Health Administration, U.S. Department of Labor.
This presentation is intended to discuss Federal Regulations only - your individual State requirements may be more stringent as many states operate their own state OSHA and they may have adopted construction standards that are different from information presented in this training. If you live in a state with an OSHA approved state plan, you should contact your local administrator for further information on the standards applicable in your state.
These materials are meant for informational purposes only.
No representation is made as to the thoroughness of the presentation.
Notes: This material was produces uner the Susan Harwood training grant number from the Occupational Safety and Health Administration under the Department of Labor.

## Slide 3: Disclaimer, cont.
It is not the intent to provide compliance-based training in this presentation, the intent is more to address hazard awareness in the residential construction (i.e. home building) industry, and to recognize the overlapping hazards present in many construction workplaces.
Photos shown in this presentation may depict situations that are not in compliance with applicable OSHA/safety requirements.
No legal advice is offered or implied, and no attorney-client relationship is intended or established. If legal advice or other expert assistance is required the services of a competent professional person should be sought.
It is the responsibility of the employer and its employees to comply with all pertinent OSHA/safety rules and regulations in the jurisdiction in which they work.
Revisions were made to this material under grant number SH05059-SH8 from the Occupational Safety and Health Administration, U.S. Department of Labor.

## Slide 4: Introduction
Falls from ladders are a leading cause of serious and fatal injuries in residential construction.
The goals of this course are to help you:
understand how to correct or eliminate fall hazards on your job sites related to ladder use.
understand the OSHA ladder safety requirements.
Notes: Falls from ladders are among the leading causes of fatalities and are a significant portion of serious injuries.

## Slide 5: Course Objectives
Identify the importance of preventing falls from ladders.
Recognize fall hazards associated with ladder use.
Identify OSHA requirements for ladders.
Identify work practices for using ladders safely.
Notes: By completing this course you will be able to: (here read each objective as it appears.)

## Slide 6: Course Agenda
Section 1: Overview
Section 2: Ladder Safety
Section 3: Group Workshop
Section 4: Post Test and Review
Notes: This course consists of four instructional sections. (Read each section as it appears on slide.)

## Slide 7: Section 1: Overview
Notes: In this section we will review:
1. The importance of ladder safety
2. Fatality statistics from the National association of Home Builders Fatality Study 2003 – 2006
3. Inspection and citation data from OSHA
4. Actual incidents involving ladders

## Slide 8: Why is Preventing Falls from Ladders Important?
Falls continue to be the leading cause of fatalities in residential construction.
Falls (602) were responsible for 45% of residential construction fatalities from 2003 to 2006.
135 (22%) were falls from ladders.
Source: NAHB Residential Construction Industry Fatalities 2003-2006 (www.nahb.org/fatalitystudy )

## Slide 9: Fatalities by Event or Exposure: Residential Construction

## Slide 10: Fall Fatalities: Residential Construction
Source: NAHB Residential Construction Industry Fatalities 2003-2006 (www.nahb.org/fatalitystudy )

## Slide 11: OSHA Fall Protection Requirements
Subpart L - 1926.451(g)
Each employee on a scaffold more than 10’ (3.1M) above a lower level shall be protected from falling to a lower level.
Subpart X – Ladders
Fall protection is not required for workers climbing or working on portable ladders.
Subpart X – Stairways
Stairways having four (4) or more risers or rising more than 30 inches must be equipped with at least one handrail; and one stair rail system along each unprotected side or edge.
Notes: Inform participants that OSHA has various requirements that address providing fall protection for workers.

## Slide 12: OSHA Fall Protection Requirements cont.
Subpart M - 1926.501(b)(13)
Residential construction. Each employee engaged in residential construction activities 6’ or more above lower levels must be protected by conventional or alternative fall protection:
Exemption: When the employer can demonstrate the protection is infeasible or creates a greater hazard the employer must develop an alternative fall protection plan.

## Slide 13: How do you prevent falls from ladders?
Implement a comprehensive safety program.
Understand OSHA ladder regulations.
Train workers to identify hazards associated with ladder use.
Use safe work practices.

## Slide 14: Ladder Safety
Section 2: Ladder Safety

## Slide 15: Learning Objectives: Section 2
Determine the proper ladder to use based on weight capacity and height.
Calculate the proper pitch of extension ladders for proper set-up, and identify how to secure and stabilize ladders.
Identify how to maintain a safe position when using a ladder.

## Slide 16: Common Ladder Hazards
Improper set-up.
Portable ladders not 3 feet above landing surface.
Not securing ladder correctly.
Standing on the top two steps of a stepladder.
Overreaching when working from a ladder.

## Slide 17: Choosing the Right Ladder
Before stepping onto a ladder, think about these things:
Duty rating of the ladder—what capacity can it hold?
Height of the ladder—too short or too tall?
Condition of the ladder and instructions unique to the ladder selected.

## Slide 18: Proper Duty Rating/Capacity
OSHA Requirement
Ladders shall not be loaded beyond the maximum intended load for which they were built nor beyond their manufacturer's rated capacity.

## Slide 19: Proper Duty Rating/Capacity, cont.
Select a ladder with the proper duty rating for your weight and the materials you are handling.

## Slide 20: Extension Ladders

## Slide 21: Proper Ladder Set-up
Consider placement and pitch of the ladder.
Secure and stabilize the ladder.

## Slide 22: Pitch Extension Ladders
Extension ladders should be used at a 4 to 1 pitch (1.2 to .3 m).
For every 4 ft. (1.2 m) in height, the bottom of the ladder should be 1 ft. (.3 m) away from the structure.
Example:
20 ft. (height) ÷ 4 ft. = 5 ft. pitch

## Slide 23: Pitch Extension Ladders, continued
Notes: Setting up extension ladders properly can reduce slip and overload hazards. A quick and easy way to determine is and extension ladder is properly set up is:
1. Place toes against ladder side rails
2. stand erect
3. Extend arms straight out
4. Palms of hands should touch top of rung at shoulder level

## Slide 24: Proper Height Extension Ladders
When accessing another level, the ladder must extend at least 3ft. (0.9m) above the landing to provide a hand hold for getting on and off the ladder.
Notes: The spikes, or spurs, on the ladder safety feet allow for the ladder to be set up safely on loose soil to prevent slipping.

## Slide 25: Proper Height for Extension Ladders, continued Choose the right ladder for the height you need to reach.
Ladder Height (ft.) | Maximum Reach (ft.)* | Height to Gutter or Top Support Point+
16 | 15 | 9 ft. max.
20 | 19 | 9-13 ft.
24 | 23 | 13-17 ft.
28 | 27 | 17-21 ft.
32 | 31 | 21-25 ft.
36 | 34 | 25-28 ft.
40 | 37 | 28-31 ft.
*Assume a 5 ft.-6 in. person with a vertical reach of 12 in.
+Support points for extension ladders reflect section overlap, ladder angle, or 3-ft. extension above roof line

## Slide 26: Secure and Stabilize Ladders
Extension ladders should be secured at the top or bottom to prevent movement.
The base of an extension ladder must be secured in place by using the safety feet on the ladder or other effective means.

## Slide 27: Secure and Stabilize Ladders, continued

## Slide 28: Secure and Stabilize Ladders - continued

## Slide 29: `Secure and Stabilize Ladders, continued

## Slide 30: Loose Soil

## Slide 31: Step Ladders

## Slide 32: Step Ladders, continued
Only use in the fully open position on firm level ground.
Do not use a step ladder that is folded or in a leaning position.
Never sit/stand on the top two rungs.
Consider work height when selecting a step ladder.

## Slide 33: Step Ladders, continued
Step ladders are designed for use in an opened-and-locked position.

## Slide 34: Step Ladders Hazard
Do NOT use a step ladder that is folded or in a leaning position.
Notes: This worker is using a stepladder in the folded, leaning position. This represents improper use of a stepladder and could possibly lead to injuries from the ladder failing.

## Slide 35: Proper Height of Stepladders
Choose a step ladder that is no more than 4ft. Shorter than the
height you want to reach.

## Slide 36: Maintain a Safe Position on Ladders
Face the ladder when ascending or descending.
Maintain three points of contact at all times.
Keep your body centered on the ladder.
Never let your belt buckle pass either side rail.

## Slide 37: Maintain a Safe Position on a Ladder

## Slide 38: Ladder Inspections
Ladders must be inspected before each use.
Broken or weak ladders or ladders that are not stable must be marked or tagged as defective and taken out of service.
Look for cracks and weak points.
Competent person must periodically inspect ladders.

## Slide 39: Ladder Inspection, continued

## Slide 40: Review the Safety Labels on the Ladder

## Slide 41: Additional Safe Work Practices: Ladders
Extension ladders should not be separated to create two ladders.
Keep the areas around the tops and bottoms of all ladders clear to prevent trip-and-fall hazards.
Avoid setting ladders up in high traffic areas or barricade the area around ladder.

## Slide 42: Additional Work Practices: Ladder Safety
Ladders must be kept free of oil, grease, and other slipping hazards.
Consider using a rope to raise/lower materials instead of carrying items while climbing a ladder.
Do NOT use metal or aluminum ladders near exposed energized electrical equipment.

## Slide 43: Workshop
Section 4:
Group Workshop

## Slide 44: Hazard Violation Workshop
Students will review a series of photographs of ladders and scaffolds in use on a jobsite. The assignment is to identify the hazards in each photo and discuss the corrective action required to correct the hazard. (Note: Some of the photos are of correct safe work practices.)
You Play OSHA!

## Slide 45: Picture #1

## Slide 46: Picture #2

## Slide 47: Picture #3
Notes: This worker is positioned on the stepladder properly. His body is centered on the ladder while performing truss installation and he is below the top two rungs.

## Slide 48: Picture #4
Notes: This worker should use a taller stepladder to reach his task. He is not using the top two steps/rungs, but he is using the backside of the ladder to increase his reach. The back side of a stepladder is not permitted for use unless designed for such use.

## Slide 49: Picture #5
Notes: Although no one is using the ladder, the metal spreader is not in the fully opened position.

## Slide 50: Picture #6
Notes: This extension ladder is properly secured at the top to prevent displacement. This is one of many ways to secure extension ladders.

## Slide 51: Picture #7
Notes: This ladder is not positioned properly. When extension ladders are being used to access another level, they must extend at least 3 feet beyond the landing surface to provide a handhold for getting on and off the ladder.

## Slide 52: Picture #8
Notes: The ladder is set up at an incorrect angle to provide access to the scaffold. The scaffolding is also set up incorrectly.

## Slide 53: Picture #9

## Slide 54: questions
Questions ?